## Slide 1
IPv6 Addressing: Learn It
Or “I was hoping to retire before I had to learn IPv6.”
Rick Graziani
CS/CIS Instructor
Cabrillo College

## Slide 2: Topics (1/3): IPv6 Address Notation, Structure and Subnetting
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 3: Topics (2/3): IPv6 Address Types
IPv6 Addressing
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80
Note: There are no broadcast addresses in IPv6

## Slide 4: Topics (3/3): Global Unicast Address Configurations
Global Unicast
IPv6 Unnumbered
Stateless Autoconfiguration
Static
EUI-64
Manual
IPv6 Address
Dynamic
DHCPv6

## Slide 5
IPv6 Address Notation, Structure and Subnetting

## Slide 6: IPv6 Address Notation
IPv6 addresses are 128-bit addresses represented in:
One Hex digit = 4 bits
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64

## Slide 7: IPv6 Address Notation
IPv6 addresses are 128-bit addresses represented in:
  Eight 16-bit segments or “hextets” (not a formal term)
One Hex digit = 4 bits
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
1 2 3 4 5 6 7 8

## Slide 8: IPv6 Address Notation
IPv6 addresses are 128-bit addresses represented in:
  Eight 16-bit segments or “hextets” (not a formal term)
  Hexadecimal (non-case sensitive) between 0000 and FFFF
  Separated by colons
One Hex digit = 4 bits
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
1 2 3 4 5 6 7 8

## Slide 9
How many addresses does 128 bits give us?
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 10
How many addresses does 128 bits give us?
  340 undecillion addesses or …
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 11
How many addresses does 128 bits give us?
  340 undecillion addesses or …
  340 trillion trillion trillion addresses or …
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 12
How many addresses does 128 bits give us?
  340 undecillion addesses or …
  340 trillion trillion trillion addresses or …
  “IPv6 could provide each and every square micrometer of the earth’s surface with 5,000 unique addresses. Micrometer = 0.001 mm or 0.000039 inches” or….
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 13
How many addresses does 128 bits give us?
  340 undecillion addesses or …
  340 trillion trillion trillion addresses or …
  “IPv6 could provide each and every square micrometer of the earth’s surface with 5,000 unique addresses. Micrometer = 0.001 mm or 0.000039 inches” or….
  “A string of soccer balls would wrap around our universe 200 billion times!” … in other words …
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 14
How many addresses does 128 bits give us?
  340 undecillion addesses or …
  340 trillion trillion trillion addresses or …
  “IPv6 could provide each and every square micrometer of the earth’s surface with 5,000 unique addresses. Micrometer = 0.001 mm or 0.000039 inches” or….
  “A string of soccer balls would wrap around our universe 200 billion times!” … in other words …
  I won’t be the one presenting IPv7 at any Cisco Academy Conference.
2001:0DB8:AAAA:1111:0000:0000:0000:0100/64
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 15: Rule 1: Leading 0’s
Two rules for reducing the size of written IPv6 addresses.
Notes:   If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeroes.

## Slide 16: Rule 1: Leading 0’s
Two rules for reducing the size of written IPv6 addresses.
The first rule is: Leading zeroes in any 16-bit segment do not have to be written.
3ffe : 0404 : 0001 : 1000 : 0000 : 0000 : 0ef0 : bc00
3ffe : 0000 : 010d : 000a : 00dd : c000 : e000 : 0001
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
Notes:   If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeroes.

## Slide 17: Rule 1: Leading 0’s
Two rules for reducing the size of written IPv6 addresses.
The first rule is: Leading zeroes in any 16-bit segment do not have to be written.
3ffe : 0404 : 0001 : 1000 : 0000 : 0000 : 0ef0 : bc00
3ffe : 404 : 1 : 1000 : 0 : 0 : ef0 : bc00
3ffe : 0000 : 010d : 000a : 00dd : c000 : e000 : 0001
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
Notes:   If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeroes.

## Slide 18: Rule 1: Leading 0’s
Two rules for reducing the size of written IPv6 addresses.
The first rule is: Leading zeroes in any 16-bit segment do not have to be written.
3ffe : 0404 : 0001 : 1000 : 0000 : 0000 : 0ef0 : bc00
3ffe : 404 : 1 : 1000 : 0 : 0 : ef0 : bc00
3ffe : 0000 : 010d : 000a : 00dd : c000 : e000 : 0001
3ffe : 0 : 10d : a : dd : c000 : e000 : 1
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
Notes:   If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeroes.

## Slide 19: Rule 1: Leading 0’s
Two rules for reducing the size of written IPv6 addresses.
The first rule is: Leading zeroes in any 16-bit segment do not have to be written.
3ffe : 0404 : 0001 : 1000 : 0000 : 0000 : 0ef0 : bc00
3ffe : 404 : 1 : 1000 : 0 : 0 : ef0 : bc00
3ffe : 0000 : 010d : 000a : 00dd : c000 : e000 : 0001
3ffe : 0 : 10d : a : dd : c000 : e000 : 1
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
ff02 : 0 : 0 : 0 : 0 : 0 : 0 : 500
Notes:   If any 16-bit segment has fewer than four hexadecimal digits, it is assumed that the missing digits are leading zeroes.

## Slide 20: Rule 2: Double colon :: equals 0000…0000
The second rule can reduce this address even further:

## Slide 21: Rule 2: Double colon :: equals 0000…0000
The second rule can reduce this address even further:
Any single, contiguous string of one or more 16-bit segments consisting of all zeroes can be represented with a double colon.
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500

## Slide 22: Rule 2: Double colon :: equals 0000…0000
The second rule can reduce this address even further:
Any single, contiguous string of one or more 16-bit segments consisting of all zeroes can be represented with a double colon.
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
ff02 : : 500
Second Rule
First Rule

## Slide 23: Rule 2: Double colon :: equals 0000…0000
The second rule can reduce this address even further:
Any single, contiguous string of one or more 16-bit segments consisting of all zeroes can be represented with a double colon.
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0500
ff02 : : 500
ff02::500
Second Rule
First Rule

## Slide 24: Rule 2: Double colon :: equals 0000…0000
Only a single contiguous string of all-zero segments can be represented with a double colon.
2001 : 0d02 : 0000 : 0000 : 0014 : 0000 : 0000 : 0095

## Slide 25: Rule 2: Double colon :: equals 0000…0000
Only a single contiguous string of all-zero segments can be represented with a double colon.
Both of these are correct…
2001 : 0d02 : 0000 : 0000 : 0014 : 0000 : 0000 : 0095
2001 : d02 :: 14 : 0 : 0 : 95
OR
2001 : d02 : 0 : 0 : 14 :: 95

## Slide 26: Rule 2: Double colon :: equals 0000…0000
Using the double colon more than once in an IPv6 address can create ambiguity because of the ambiguity in the number of 0’s.
2001:d02::14::95

## Slide 27: Rule 2: Double colon :: equals 0000…0000
Using the double colon more than once in an IPv6 address can create ambiguity because of the ambiguity in the number of 0’s.
2001:d02::14::95
2001:0d02:0000:0000:0014:0000:0000:0095
2001:0d02:0000:0000:0000:0014:0000:0095
2001:0d02:0000:0014:0000:0000:0000:0095

## Slide 28: Network Prefixes
IPv4, the prefix—the network portion of the address—can be identified by a dotted decimal netmask or bitcount.
255.255.255.0 or /24
Notes: The address is followed by a forward slash and a decimal number indicating how many of the first bits of the address are the prefix bits.

## Slide 29: Network Prefixes
IPv4, the prefix—the network portion of the address—can be identified by a dotted decimal netmask or bitcount.
255.255.255.0 or /24
IPv6 prefixes are always identified by bitcount (prefix length).
Notes: The address is followed by a forward slash and a decimal number indicating how many of the first bits of the address are the prefix bits.

## Slide 30: Network Prefixes
IPv4, the prefix—the network portion of the address—can be identified by a dotted decimal netmask or bitcount.
255.255.255.0 or /24
IPv6 prefixes are always identified by bitcount (prefix length).
Prefix length notation:
3ffe:1944:100:a::/64
Notes: The address is followed by a forward slash and a decimal number indicating how many of the first bits of the address are the prefix bits.

## Slide 31: Network Prefixes
IPv4, the prefix—the network portion of the address—can be identified by a dotted decimal netmask or bitcount.
255.255.255.0 or /24
IPv6 prefixes are always identified by bitcount (prefix length).
Prefix length notation:
3ffe:1944:100:a::/64
16 32 48 64 bits
Notes: The address is followed by a forward slash and a decimal number indicating how many of the first bits of the address are the prefix bits.

## Slide 32
IPv6 Address Types

## Slide 33
IPv6 Addressing
IPv6 Address Types: Starting with Global Unicast
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80
Note: There are no broadcast addresses in IPv6

## Slide 34
Interface ID
Subnet ID
Global Routing Prefix
Structure of a Global Unicast Address
n bits
m bits
128-n-m bits
Global unicast addresses are similar to IPv4 addresses.

## Slide 35
Interface ID
Subnet ID
Global Routing Prefix
Structure of a Global Unicast Address
n bits
m bits
128-n-m bits
Global unicast addresses are similar to IPv4 addresses.
  Routable
  Unique

## Slide 36
Interface ID
Subnet ID
Global Routing Prefix
Structure of a Global Unicast Address
n bits
m bits
128-n-m bits
001
Range 2000::/3 to 3FFF::/3 (4th bit can be a 0 or a 1)
Global unicast addresses are similar to IPv4 addresses.
  Routable
  Unique

## Slide 37
Interface ID
Subnet ID
Global Routing Prefix
Structure of a Global Unicast Address
n bits
m bits
128-n-m bits
001
IANA’s allocation of IPv6 address space in 1/8th sections
Global unicast addresses are similar to IPv4 addresses.
  Routable
  Unique
Range 2000::/3 to 3FFF::/3 (4th bit can be a 0 or a 1)

## Slide 38
Global Unicast Addresses and the 3-1-4 rule
IPv4 Unicast Address
32 bits
Network portion
Host portion
Subnet portion

## Slide 39
Global Unicast Addresses and the 3-1-4 rule
IPv4 Unicast Address
32 bits
Network portion
Host portion
Subnet portion
/?

## Slide 40
Global Unicast Addresses and the 3-1-4 rule
IPv4 Unicast Address
32 bits
Network portion
Host portion
Subnet portion
IPv6 Global Unicast Address
128 bits
Global Routing Prefix
Interface ID
/?

## Slide 41
Global Unicast Addresses and the 3-1-4 rule
IPv4 Unicast Address
32 bits
Network portion
Host portion
Subnet portion
IPv6 Global Unicast Address
128 bits
Global Routing Prefix
Interface ID
/64
/?
* 64-bit Interface ID gives us 18 quintillion (18,446,744,073,709,551,616) devices/subnet.
* Supports 48bit and 64-bit MAC addresses as the Interface ID (coming).

## Slide 42
Global Unicast Addresses and the 3-1-4 rule
IPv4 Unicast Address
32 bits
Network portion
Host portion
Subnet portion
IPv6 Global Unicast Address
128 bits
Global Routing Prefix
Interface ID
Fixed 16-bit Subnet ID
/64
/?
* 64-bit Interface ID gives us 18 quintillion (18,446,744,073,709,551,616) devices/subnet.
* 16-bit Subnet ID gives us 65,536 subnets. (Yes, you can use the all 0’s and all 1’s.) 
/48

## Slide 43
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100

## Slide 44
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits

## Slide 45
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
/48

## Slide 46
Subnet ID
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
/48
/64

## Slide 47
Interface ID
Subnet ID
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
/48
/64

## Slide 48
Interface ID
Subnet ID
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
3
/48
/64

## Slide 49
Interface ID
Subnet ID
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
3
1
/48
/64

## Slide 50
Interface ID
Subnet ID
Global Routing Prefix
Global Unicast Addresses and the 3-1-4 rule
2001 : 0DB8 : AAAA : 1111 : 0000 : 0000 : 0000 : 0100
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
16 bits
3
1
4
/48
/64

## Slide 51
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix

## Slide 52
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix
/23
*RIR
* This is a minimum allocation. The prefix-length may be less if it can be justified.

## Slide 53
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix
/32
/23
*RIR
*ISP Prefix
* This is a minimum allocation. The prefix-length may be less if it can be justified.

## Slide 54
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix
/48
/32
/23
*RIR
*ISP Prefix
*Site Prefix
* This is a minimum allocation. The prefix-length may be less if it can be justified.
16-bit Subnet ID

## Slide 55
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix
/48
/32
/23
*RIR
*ISP Prefix
*Site Prefix
* This is a minimum allocation. The prefix-length may be less if it can be justified.
/56
Possible Home Site Prefix
8-bit Subnet ID

## Slide 56
Global Routing Prefix Sizes
Interface ID
Subnet ID
Global Routing Prefix
/48
/64
/32
/23
*RIR
*ISP Prefix
*Site Prefix
Subnet Prefix
* This is a minimum allocation. The prefix-length may be less if it can be justified.
/56
Possible Home Site Prefix

## Slide 57: Subnetting IPv6
4 specific subnets could be:
2340:1111:AAAA::/48

## Slide 58: Subnetting IPv6
4 specific subnets could be:
  2340:1111:AAAA:0000::/64
  2340:1111:AAAA:0001::/64
  2340:1111:AAAA:0002::/64
  2340:1111:AAAA:000A::/64
Note: A valid abbreviation is to remove the 3 leading 0’s from the first shown quartet.
  2340:1111:AAAA:1::/64
2340:1111:AAAA::/48
Just increment by 1 in hex

## Slide 59
Interface ID
Subnet ID
Global Routing Prefix
Subnetting into the Interface ID
Prefix
64 bits
48 bits
16bits
/48
/112
2001 : 0DB8 : AAAA : 0000 : 0000 : 0000 : 0000 : 0000
2001 : 0DB8 : AAAA : 0000 : 0000 : 0000 : 0001 : 0000
2001 : 0DB8 : AAAA : 0000 : 0000 : 0000 : 0002 : 0000
thru
2001 : 0DB8 : AAAA : FFFF : FFFF : FFFF : FFFE : 0000
2001 : 0DB8 : AAAA : FFFF : FFFF : FFFF : FFFF : 0000
Global Routing Prefix
Subnet-ID
Interface ID

## Slide 60
Subnetting on a nibble boundary
Interface ID
Subnet ID
Global Routing Prefix
Subnet Prefix
/68
60 bits
48 bits
20 bits
/48
/68
  Subnetting on a nibble (4 bit) boundary makes it easier to list the subnets:
  /64, /68, /72, etc.
  2001:0DB8:AAAA:0000:0000::/68
  2001:0DB8:AAAA:0000:1000::/68
  2001:0DB8:AAAA:0000:2000::/68 through
  2001:0DB8:AAAA:FFFF:F000::/68
Just increment by 1 in hex

## Slide 61
Subnetting within a nibble
Interface ID
Subnet ID
Global Routing Prefix
Subnet Prefix
/70
58 bits
48 bits
22 bits
/48
/70
  2001:0DB8:AAAA:0000:0000::/70 0000
  2001:0DB8:AAAA:0000:0400::/70 0100
  2001:0DB8:AAAA:0000:0800::/70 1000
  2001:0DB8:AAAA:0000:0C00::/70 1100
Four Bits: The two leftmost bits are part of the Subnet-ID, whereas the two rightmost bits belong to the Interface ID.
bits

## Slide 62
IPv6 Addressing
IPv6 Address Types: Global Unicast
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80
Note: There are no broadcast addresses in IPv6

## Slide 63
Global Unicast
Static Global Unicast Addresses
Dynamic
IPv6 Unnumbered
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
Manual
IPv6 Address

## Slide 64
Rick’s Café Network Topology
PC-1
PC-2
PC-3
PC-4
R2
R3
ISP
R1
Ser 0/0/0
.1
Ser 0/0/0
.2
Ser 0/0/0
.2
Ser 0/0/0
.2
Ser 0/0/1
.1
Ser 0/0/1
.2
Ser 0/0/
.1
Ser 0/0/1
.1
Fa 0/0
Fa 0/0
Fa 0/0
Fa 0/0
2001:0DB8:CAFE:0002::/64
Rick’s Cafe
2001:0DB8:CAFE::/48
2001:0DB8:CAFE:0001::/64
2001:0DB8:CAFE:0003::/64
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:A002::/64
2001:0DB8:CAFE:A003::/64
2001:0DB8:FEED:0001::/64
Link to ISP
2001:0DB8:FACE:C0DE::/64

## Slide 65
R1# conf t
R1(config)# interface fastethernet 0/0
Configuring a Static Global Unicast Address
Exactly the same as an IPv4 address only different.

## Slide 66
R1# conf t
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::1/64
Configuring a Static Global Unicast Address
Exactly the same as an IPv4 address only different.
No space between IPv6 address and Prefix-length.
No space

## Slide 67
R1# conf t
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::1/64
R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)#
Configuring a Static Global Unicast Address
Exactly the same as an IPv4 address only different.
No space between IPv6 address and Prefix-length.
No space

## Slide 68
R1# conf t
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::1/64
R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)#
Configuring a Static Global Unicast Address
Exactly the same as an IPv4 address only different.
No space between IPv6 address and Prefix-length.
IOS commands for IPv6 are very similar to their IPv4 counterpart.
No space

## Slide 69
R1# conf t
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::1/64
R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)#
Configuring a Static Global Unicast Address
Exactly the same as an IPv4 address only different.
No space between IPv6 address and Prefix-length.
IOS commands for IPv6 are very similar to their IPv4 counterpart.
All 0’s and all 1’s are valid IPv6 host IPv6 addresses.
No space

## Slide 70
show running-config command on router R1
R1# show running-config
<output omitted for brevity>
interface FastEthernet0/0
no ip address
duplex auto
speed auto
ipv6 address 2001:DB8:CAFE:1::1/64
!

## Slide 71
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief

## Slide 72
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:1::1
R1#
Global unicast address

## Slide 73
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:1::1
R1#
Global unicast address
Link-local unicast address
Link-local address automatically created when (before) the global unicast address is.

## Slide 74
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:1::1
R1#
Global unicast address
Link-local unicast address
Link-local address automatically created when (before) the global unicast address is.
We will discuss link-local addresses next.

## Slide 75
show ipv6 interface fastethernet 0/0 command on R1
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:CAFE:1::1, subnet is 2001:DB8:CAFE:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFC2:828D
MTU is 1500 bytes
<output omitted for brevity>
R1#

## Slide 76
PC-1: Static Global Unicast Address

## Slide 77
PC-1: Static Global Unicast Address

## Slide 78
PC1> ipconfig
Windows IP Configuration
Ethernet adapter Local Area Connection:
Connection-specific DNS Suffix . :
IPv6 Address. . . . . . . . . . . : 2001:db8:cafe:1::100
Link-local IPv6 Address . . . . . : fe80::50a5:8a35:a5bb:66e1%11
Default Gateway . . . . . . . . . : 2001:db8:cafe:1::1
PC-1: Static Global Unicast Address

## Slide 79
Global Unicast
Dynamic
IPv6 Unnumbered
IPv6 Address
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
Modified EUI-64 Format: Creates a 64-bit Interface ID from a 48-bit MAC address
Manual

## Slide 80
R1(config)# interface fastethernet 0/0
Router’s global unicast address can be configured with:
  Statically configured prefix and …
2001:0DB8:CAFE:1::/64
Fa0/0
R1
Global Unicast:
Prefix: 2001:0DB8:AAAA:1::/64
Interface ID: EUI-64

## Slide 81
R1(config)# interface fastethernet 0/0
Router’s global unicast address can be configured with:
  Statically configured prefix and …
  EUI-64 generated Interface ID
2001:0DB8:CAFE:1::/64
Fa0/0
R1
Global Unicast:
Prefix: 2001:0DB8:AAAA:1::/64
Interface ID: EUI-64

## Slide 82
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::/64 ?
Router’s global unicast address can be configured with:
  Statically configured prefix and …
  EUI-64 generated Interface ID
2001:0DB8:CAFE:1::/64
Fa0/0
R1
Global Unicast:
Prefix: 2001:0DB8:AAAA:1::/64
Interface ID: EUI-64

## Slide 83
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::/64 ?
eui-64 Use eui-64 interface identifier
<cr> <<< All0’s address is okay!
Router’s global unicast address can be configured with:
  Statically configured prefix and …
  EUI-64 generated Interface ID
2001:0DB8:CAFE:1::/64
Fa0/0
R1
Global Unicast:
Prefix: 2001:0DB8:AAAA:1::/64
Interface ID: EUI-64

## Slide 84
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::/64 ?
eui-64 Use eui-64 interface identifier
<cr> <<< All0’s address is okay!
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::/64 eui-64
R1(config-if)#
Router’s global unicast address can be configured with:
  Statically configured prefix and …
  EUI-64 generated Interface ID
2001:0DB8:CAFE:1::/64
Fa0/0
R1
Global Unicast:
Prefix: 2001:0DB8:AAAA:1::/64
Interface ID: EUI-64

## Slide 85
R1# show interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Hardware is AmdFE, address is 0003.6be9.d480 (bia 0003.6be9.d480)
<output omitted for brevity>
Ethernet MAC address
R1’s MAC Address for FastEthernet 0/0

## Slide 86
R1# show interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Hardware is AmdFE, address is 0003.6be9.d480 (bia 0003.6be9.d480)
<output omitted for brevity>
Ethernet MAC address
R1’s MAC Address for FastEthernet 0/0
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
00
03
6B
E9
D4
80
Binary
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000

## Slide 87
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
Modified EUI-64 Format

## Slide 88
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
Binary
Step 2: Insert FFFE
1111 1111
1111 1110
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
0000 0000
0000 0011
0110 1011
Modified EUI-64 Format
F F F E

## Slide 89
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
Binary
Step 2: Insert FFFE
Binary
Step 3: Flip the U/L bit
1111 1111
1111 1110
1111 1111
1111 1110
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
0000 0000
0000 0011
0110 1011
0000 0010
0000 0011
0110 1011
Modified EUI-64 Format
F F F E

## Slide 90
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
Binary
Step 2: Insert FFFE
Binary
Step 3: Flip the U/L bit
Binary
Modified EUI-64 Interface ID in Hexadecimal Notation
1111 1111
1111 1110
1111 1111
1111 1110
02
03
6B
E9
D4
80
FF
FE
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
0000 0000
0000 0011
0110 1011
0000 0010
0000 0011
0110 1011
Modified EUI-64 Format
F F F E

## Slide 91
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
Configuring IPv6 address on Fa 0/0 using EUI-64 format

## Slide 92
Configuring IPv6 address on Fa 0/0 using EUI-64 format
0 0 0 3 . 6 b e 9 . D 4 8 0
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0000 0010 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0 2 0 3 . 6 b F F F E e 9 . D 4 8 0
1
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
2
3

## Slide 93
Configuring IPv6 address on Fa 0/0 using EUI-64 format
0 0 0 3 . 6 b e 9 . D 4 8 0
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0000 0010 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0 2 0 3 . 6 b F F F E e 9 . D 4 8 0
1
Global unicast address: 2001:0DB8:AAAA:0001:0203:6BFF:FEE9:D480
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
2
3

## Slide 94
Configuring IPv6 address on Fa 0/0 using EUI-64 format
0 0 0 3 . 6 b e 9 . D 4 8 0
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0000 0010 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0 2 0 3 . 6 b F F F E e 9 . D 4 8 0
1
Interface ID (EUI-64 format)
Global unicast address: 2001:0DB8:AAAA:0001:0203:6BFF:FEE9:D480
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
2
3

## Slide 95
Configuring IPv6 address on Fa 0/0 using EUI-64 format
0 0 0 3 . 6 b e 9 . D 4 8 0
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 1110 1001 . 0111 0100 1000 0000
0000 0000 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0000 0010 0000 0011 . 0110 1011 11111111 11111110 1110 1001 . 0111 0100 1000 0000
0 2 0 3 . 6 b F F F E e 9 . D 4 8 0
1
Interface ID (EUI-64 format)
Subnet Prefix (Manually configured)
Global unicast address: 2001:0DB8:AAAA:0001:0203:6BFF:FEE9:D480
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
2
3

## Slide 96
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:aaaa:0001::/64 eui-64
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:CAFE:1:203:6BFF:FEE9:D480,
subnet is 2001:DB8:CAFE:1::/64
<output omitted for brevity>
Address using EUI-64 format

## Slide 97
Dynamic Global Unicast Addresses

## Slide 98
Global Unicast
Manual
IPv6 Unnumbered
IPv6 Address
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
Dynamic

## Slide 99: Stateless Address Autoconfiguration (SLAAC)
Stateless Address Autoconfiguration (SLAAC) is an automatic method for assigning global unicast addresses to interfaces.
No need for DHCPv6 server
NDP Router Solicitation
ipv6 unicast-routing
1
2
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64
NDP Router Advertisement

## Slide 100
ipv6 unicast-routing
R1
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Router Solicitation and Router Advertisement messages are about communications between a host and a router.
NDP Router Advertisement
NDP Router Solicitation “Need information from the router”

## Slide 101
ipv6 unicast-routing
R1
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Router Solicitation and Router Advertisement messages are about communications between a host and a router.
Part of ICMPv6’s Neighbor Discovery Protocol
NDP Router Advertisement
NDP Router Solicitation “Need information from the router”

## Slide 102
ipv6 unicast-routing
R1
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Router Solicitation and Router Advertisement messages are about communications between a host and a router.
Part of ICMPv6’s Neighbor Discovery Protocol
Routers periodically send Router Advertisement messages or response to a Router Solicitation message from a host on the link.
NDP Router Advertisement
NDP Router Solicitation “Need information from the router”

## Slide 103
ipv6 unicast-routing
RouterA
DHCPv6 Server
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.

## Slide 104
ipv6 unicast-routing
RouterA
DHCPv6 Server
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.
ipv6 unicast-routing command enables router to send Router Advertisements.
RouterA(config)# ipv6 unicast-routing

## Slide 105
ipv6 unicast-routing
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
Router Advertisements are sent periodically (Cisco default every 200 seconds)
Or in response to a Router Solicitation message.

## Slide 106
ipv6 unicast-routing
2
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
Router Advertisements are sent periodically (Cisco default every 200 seconds)
Or in response to a Router Solicitation message.
NDP Router Advertisement

## Slide 107
ipv6 unicast-routing
2
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.
NDP Router Advertisement
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”

## Slide 108
ipv6 unicast-routing
2
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.
NDP Router Advertisement
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Or
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”

## Slide 109
ipv6 unicast-routing
2
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.
NDP Router Advertisement
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Or
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Or
“I can’t help you. Ask a DHCPv6 server for all your information.”

## Slide 110
ipv6 unicast-routing
2
RouterA
DHCPv6 Server
NDP Router Solicitation “Need information from the router”
1
The router’s Router Advertisement can determine how the host gets its dynamic address configuration.
NDP Router Advertisement
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Or
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Or
“I can’t help you. Ask a DHCPv6 server for all your information.”
More detail in ICMPv6 Session!

## Slide 111
NDP Router Solicitation
ipv6 unicast-routing
1
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64

## Slide 112
NDP Router Advertisement
From: FE80::1 (Link-local address)
NDP Router Solicitation
ipv6 unicast-routing
1
2
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64

## Slide 113
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
NDP Router Solicitation
ipv6 unicast-routing
1
2
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64

## Slide 114
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
NDP Router Solicitation
ipv6 unicast-routing
1
2
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64

## Slide 115
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
MAC: 00-19-D2-8C-E0-4C
RouterA
EUI-64

## Slide 116
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
MAC: 00-19-D2-8C-E0-4C
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
RouterA
EUI-64

## Slide 117
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
MAC: 00-19-D2-8C-E0-4C
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
EUI-64 Interface ID: 02-19-D2-FF-FE-8C-E0-4C
RouterA
EUI-64

## Slide 118
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
MAC: 00-19-D2-8C-E0-4C
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
EUI-64 Interface ID: 02-19-D2-FF-FE-8C-E0-4C
Global Unicast Address:
2001:DB8:AAAA:1:0219:D2FF:FE8C:E04C
RouterA
EUI-64

## Slide 119
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
MAC: 00-19-D2-8C-E0-4C
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
EUI-64 Interface ID: 02-19-D2-FF-FE-8C-E0-4C
Global Unicast Address:
2001:DB8:AAAA:1:0219:D2FF:FE8C:E04C
Default Gateway: FE80::1
RouterA
EUI-64

## Slide 120
NDP Router Advertisement
From: FE80::1 (Link-local address)
To: FF02::1 (All-hosts multicast)
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
MAC: 00-19-D2-8C-E0-4C
Prefix: 2001:DB8:AAAA:1::
Prefix-length: /64
EUI-64 Interface ID: 02-19-D2-FF-FE-8C-E0-4C
Global Unicast Address:
2001:DB8:AAAA:1:0219:D2FF:FE8C:E04C
Default Gateway: FE80::1
PC1> ipconfig
IPv6 Address. . . . . . : 2001:DB8:AAAA:1:0219:D2FF:FE8C:E04C
Default Gateway . . . . : fe80::1
RouterA
EUI-64

## Slide 121
PC1> ipconfig
Windows IP Configuration
Ethernet adapter Local Area Connection:
IPv6 Address. . . . . . . . . : 2001:DB8:AAAA:1:0219:D2FF:FE8C:E04C
Link-local IPv6 Address . . . : fe80::50a5:8a35:a5bb:66e1%11
Default Gateway . . . . . . . : fe80::1
Windows and the Interface ID
Windows XP and Server 2003 use EUI-64.
Windows Vista and newer do not use EUI-64; hosts create a random 64-bit Interface ID.
The %value following the link-local address is a Windows Zone ID and not part of IPv6.

## Slide 122
NDP Router Advertisement
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Or
“I can’t help you. Ask a DHCPv6 server for all your information.”
NDP Router Solicitation
ipv6 unicast-routing
1
RouterA
DHCPv6 Server
Stateless Addressing
2

## Slide 123
NDP Router Advertisement
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Or
“I can’t help you. Ask a DHCPv6 server for all your information.”
NDP Router Solicitation
ipv6 unicast-routing
1
2
3
RouterA
4
DHCPv6 Advertise Message
“I’m a DHCPv6 Server.”
DHCPv6 Solicit Message
“I need a DHCPv6 Server.”
DHCPv6 Server
5
DHCPv6 Request Message
“I need addressing information.
6
DHCPv6 Reply Message
“Here is your address and other information.”
Stateless Addressing
DHCPv6 Addressing

## Slide 124
Global Unicast
Manual
IPv6 Unnumbered
IPv6 Address
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
“Stateful DHCPv6”
Dynamic

## Slide 125
ipv6 unicast-routing
1
RouterA
2
DHCPv6 Advertise Message
“I’m a DHCPv6 Server.”
DHCPv6 Solicit Message
“I need a DHCPv6 Server.”
DHCPv6 Server
3
DHCPv6 Request Message
“I need addressing information.
4
DHCPv6 Reply Message
“Here is your address and other information.”
DHCPv6 Addressing
“Stateful DHCPv6”

## Slide 126
We looked at all the different options for configuring a global unicast address except for IPv6 unnumbered which is similar to the IPv4 unnumbered.
Global Unicast
IPv6 Unnumbered
Stateless Autoconfiguration
Static
EUI-64
Manual
IPv6 Address
Dynamic
DHCPv6

## Slide 127
Link-local Unicast Address

## Slide 128
IPv6 Addressing
Link-Local Unicast
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80

## Slide 129
Range:
FE80::/10
FEBF::/10
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 130
Range:
FE80::/10
FEBF::/10
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 131
Used to communicate with other devices on the link.
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 132
Used to communicate with other devices on the link.
Are NOT routable off the link.
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 133
Used to communicate with other devices on the link.
Are NOT routable off the link.
An IPv6 device must have at least a link-local address.
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 134
Used to communicate with other devices on the link.
Are NOT routable off the link.
An IPv6 device must have at least a link-local address.
Used by:
  Hosts to communicate to the IPv6 network before it has a global unicast address.
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 135
Used to communicate with other devices on the link.
Are NOT routable off the link.
An IPv6 device must have at least a link-local address.
Used by:
  Hosts to communicate to the IPv6 network before it has a global unicast address.
  Used as the default gateway address by hosts.
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 136
Used to communicate with other devices on the link.
Are NOT routable off the link.
An IPv6 device must have at least a link-local address.
Used by:
  Hosts to communicate to the IPv6 network before it has a global unicast address.
  Used as the default gateway address by hosts.
  Adjacent routers to exchange routing updates
Interface ID
/64
1111 1110 10xx xxxx
FE80::/10
Remaining 54 bits
10 bits
64 bits
EUI-64, Random or Manual Configuration
Link-local unicast

## Slide 137
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Link-local address automatically created when (before) the global unicast address is.
Link-local address: ?
Link-local address: ?
PC-1
R2
R1

## Slide 138
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Link-local address automatically created when (before) the global unicast address is.
FE80 + 64-bit Interface ID
  EUI-64 Format or
  Randomly generated
Link-local address: ?
Link-local address: ?
PC-1
R2
R1

## Slide 139
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Link-local address automatically created when (before) the global unicast address is.
FE80 + 64-bit Interface ID
  EUI-64 Format
  Randomly generated
Link-local address can also be created statically.
Link-local address: ?
Link-local address: ?
PC-1
R2
R1

## Slide 140
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:1::1
Serial0/0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:A001::1
Serial0/0/1 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:A003::1
R1#
Link-local address automatically created when (before) the global unicast address.
Global unicast address
Link-local unicast address

## Slide 141
show ipv6 interface brief command on router R1
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:1::1
Serial0/0/0 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:A001::1
Serial0/0/1 [up/up]
FE80::203:6BFF:FEE9:D480
2001:DB8:CAFE:A003::1
R1#
Link-local address automatically created when (before) the global unicast address.
By default, IOS will use modified EUI-64 format.
Global unicast address
Link-local unicast address

## Slide 142
R1# show interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Hardware is AmdFE, address is 0003.6be9.d480 (bia 0003.6be9.d480)
<output omitted for brevity>
Ethernet MAC address

## Slide 143
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
Binary
Step 2: Insert FFFE
Binary
Step 3: Flip the U/L bit
Binary
Modified EUI-64 Interface ID in Hexadecimal Notation
1111 1111
1111 1110
1111 1111
1111 1110
02
03
6B
E9
D4
80
FF
FE
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
0000 0000
0000 0011
0110 1011
0000 0010
0000 0011
0110 1011
Modified EUI-64 Format

## Slide 144
R1# show interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
Hardware is AmdFE, address is 0003.6be9.d480 (bia 0003.6be9.d480)
<output omitted for brevity>
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
<output omitted for brevity>
Link-local address using EUI-64 format
Ethernet MAC address

## Slide 145
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Dynamic link-local addresses can be difficult to identify.
PC-1
R2
R1
FE80::203:6BFF:FEE9:D480
(EUI-64)
FE80::50A5:8A35:A5BB:66E1

## Slide 146
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Dynamic link-local addresses can be difficult to identify.
Routers use link-local addresses for:
  Exchanging routing updates
  Default gateway address for hosts
PC-1
R2
R1
FE80::203:6BFF:FEE9:D480
(EUI-64)
FE80::50A5:8A35:A5BB:66E1

## Slide 147
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Dynamic link-local addresses can be difficult to identify.
Routers use link-local addresses for:
  Exchanging routing updates
  Default gateway address for hosts
Static link-local addresses are easier to remember and identify.
PC-1
R2
R1
FE80::203:6BFF:FEE9:D480
(EUI-64)
FE80::50A5:8A35:A5BB:66E1
FE80::1
(Static)

## Slide 148
Global Unicast:
2001:0DB8:CAFE:1::0100
2001:0DB8:CAFE:A001::/64
2001:0DB8:CAFE:1::/64
Fa0/0
Ser 0/0/0
.1
Ser 0/0/0
.2
Global Unicast:
2001:0DB8:CAFE:1::1/64
Dynamic link-local addresses can be difficult to identify.
Routers use link-local addresses for:
  Exchanging routing updates
  Default gateway address for hosts
Static link-local addresses are easier to remember and identify.
Link-local addresses only have to be unique on the link!
PC-1
R2
R1
FE80::203:6BFF:FEE9:D480
(EUI-64)
FE80::50A5:8A35:A5BB:66E1
FE80::1
(Static)

## Slide 149
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 ?
link-local Use link-local address
R1(config)#
Static Link-local Address

## Slide 150
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 ?
link-local Use link-local address
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# exit
R1(config)#
Static Link-local Address

## Slide 151
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 ?
link-local Use link-local address
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# exit
R1(config)# interface serial 0/0/0
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# exit
R1#
Static Link-local Address

## Slide 152
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 ?
link-local Use link-local address
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# exit
R1(config)# interface serial 0/0/0
R1(config-if)# ipv6 address fe80::1 link-local
R1(config-if)# exit
R1#
R1# show ipv6 interface brief
FastEthernet0/0 [up/up]
FE80::1
2001:DB8:CAFE:1::1
Serial0/0/0 [up/up]
FE80::1
2001:DB8:CAFE:A001::1
R1#
Same link-local unicast address (best practice)
Static Link-local Address

## Slide 153
R1# show running-config
!
interface FastEthernet0/0
no ip address
ipv6 address FE80::1 link-local
ipv6 address 2001:DB8:CAFE:1::1/64
!
interface Serial0/0/0
no ip address
ipv6 address FE80::1 link-local
ipv6 address 2001:DB8:CAFE:A001::1/64
!

## Slide 154
R1# ping fe80::2
Fa0/0
Global Unicast:
2001:0DB8:CAFE:1::1/64
FE80::1
2001:0DB8:CAFE:A001::/64
Ser 0/0/0
.1
Ser 0/0/0
.2
R2
R1
FE80::1
FE80::2
Ping Link-local Address

## Slide 155
R1# ping fe80::2
Output Interface: ser 0/0/0
Must include exit-interface
Fa0/0
Global Unicast:
2001:0DB8:CAFE:1::1/64
FE80::1
2001:0DB8:CAFE:A001::/64
Ser 0/0/0
.1
Ser 0/0/0
.2
R2
R1
FE80::1
FE80::2
Ping Link-local Address

## Slide 156
R1# ping fe80::2
Output Interface: ser 0/0/0
% Invalid interface. Use full interface name without spaces (e.g. Serial0/1)
Output Interface: serial0/0/0
Must include exit-interface
Fa0/0
Global Unicast:
2001:0DB8:CAFE:1::1/64
FE80::1
2001:0DB8:CAFE:A001::/64
Ser 0/0/0
.1
Ser 0/0/0
.2
R2
R1
FE80::1
FE80::2
Ping Link-local Address

## Slide 157
R1# ping fe80::2
Output Interface: ser 0/0/0
% Invalid interface. Use full interface name without spaces (e.g. Serial0/1)
Output Interface: serial0/0/0
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to FE80::2, timeout is 2 secs:
!!!!!
Must include exit-interface
Fa0/0
Global Unicast:
2001:0DB8:CAFE:1::1/64
FE80::1
2001:0DB8:CAFE:A001::/64
Ser 0/0/0
.1
Ser 0/0/0
.2
R2
R1
FE80::1
FE80::2
Ping Link-local Address

## Slide 158
ipv6 enable command
Router(config)# interface fastethernet 0/1
Link-local addresses are automatically created whenever a global unicast address is configured.

## Slide 159
ipv6 enable command
Router(config)# interface fastethernet 0/1
Router(config-if)# ipv6 enable
Router(config-if)# end
Router#
Link-local addresses are automatically created whenever a global unicast address is configured.
The ipv6 enable command will:

## Slide 160
ipv6 enable command
Router(config)# interface fastethernet 0/1
Router(config-if)# ipv6 enable
Router(config-if)# end
Router#
Link-local addresses are automatically created whenever a global unicast address is configured.
The ipv6 enable command will:
  Create a link-local address when there is no global unicast address

## Slide 161
ipv6 enable command
Router(config)# interface fastethernet 0/1
Router(config-if)# ipv6 enable
Router(config-if)# end
Router# show ipv6 interface brief
FastEthernet0/1 [up/up]
FE80::20C:30FF:FE10:92E1
Router#
Link-local addresses are automatically created whenever a global unicast address is configured.
The ipv6 enable command will:
  Create a link-local address when there is no global unicast address
Link-local unicast address only

## Slide 162
ipv6 enable command
Router(config)# interface fastethernet 0/1
Router(config-if)# ipv6 enable
Router(config-if)# end
Router# show ipv6 interface brief
FastEthernet0/1 [up/up]
FE80::20C:30FF:FE10:92E1
Router#
Link-local addresses are automatically created whenever a global unicast address is configured.
The ipv6 enable command will:
  Create a link-local address when there is no global unicast address
  Maintain the link-local address even when the global unicast address is removed.
Link-local unicast address only

## Slide 163
PC1> ipconfig
Windows IP Configuration
Ethernet adapter Local Area Connection:
Connection-specific DNS Suffix . :
IPv6 Address. . . . . . . . . . . : 2001:db8:cafe:1::100
Link-local IPv6 Address . . . . . : fe80::50a5:8a35:a5bb:66e1%11
Default Gateway . . . . . . . . . : 2001:db8:cafe:1::1
Windows Link-local address
Windows operating systems, Windows XP and Server 2003 use EUI-64.
Windows Vista and newer do not use EUI-64 create a random 64-bit Interface ID.
The %value following the link-local address is a Windows Zone ID and not part of IPv6.

## Slide 164
Mymac$ ifconfig
en0: flags=8863<UP,BROADCAST,SMART,RUNNING,SIMPLEX,MULTICAST> mtu 1500
ether c4:2c:03:2a:b5:a2
inet6 fe80::c62c:3ff:fe2a:b5a2
MAC Link-local address
My MAC OS 10.6 uses EUI-64 but you check with your OS flavor and version.
Many Linux flavors moving to random Interface IDs

## Slide 165
IPv6 Addressing
Other Unicast Addresses
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80

## Slide 166
Multicast Addresses

## Slide 167
IPv6 Addressing
Multicast Addresses
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80
Similar to IPv4 multicast – one-to-many addressing

## Slide 168
Group ID
Flag
1111 1111
FF00::/8
8 bits
112bits
4 bits
4 bits
Scope
Flag
  0 Permanent, well-known multicast address assigned by IANA
  1 Non-permanently-assigned, “dynamically" assigned multicast address
Scope (partial list)
  0 Reserved
  1 Interface-Local scope
  2 Link-Local scope
  5 Site-Local scope
  8 Organization-Local scope

## Slide 169
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
All-nodes on this link (Assigned)
Member of these Multicast Groups
FF02 – “2” means link-local scope

## Slide 170
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
All-nodes on this link (Assigned)
All-routers on this link: IPv6 routing enabled (Assigned)
Member of these Multicast Groups
FF02 – “2” means link-local scope

## Slide 171
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
All-nodes on this link (Assigned)
All-routers on this link: IPv6 routing enabled (Assigned)
Solicited-node multicast address for Global Address
Member of these Multicast Groups
FF02 – “2” means link-local scope

## Slide 172
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
All-nodes on this link (Assigned)
All-routers on this link: IPv6 routing enabled (Assigned)
Solicited-node multicast address for Link-local Unicast Address
Solicited-node multicast address for Global Address
Member of these Multicast Groups
FF02 – “2” means link-local scope
What is Solicited node? (coming)

## Slide 173
Enabling IPv6 Routing
R1(config)# interface fastethernet 0/0
R1(config-if)# ipv6 address 2001:0db8:cafe:0001::1/64
A router’s interfaces can be enabled (get an IPv6 address) for IPv6 like any other device on the network.

## Slide 174
Enabling IPv6 Routing
R1(config)# ipv6 unicast-routing
R1# show ipv6 interface fastethernet 0/0
Joined group address(es):
FF02::2
A router’s interfaces can be enabled (get an IPv6 address) for IPv6 like any other device on the network.
For the router to “act” as an IPv6 router it must be enabled with the ipv6-unicast routing command.
All-routers on this link (Assigned)

## Slide 175
Enabling IPv6 Routing
R1(config)# ipv6 unicast-routing
R1# show ipv6 interface fastethernet 0/0
Joined group address(es):
FF02::2
A router’s interfaces can be enabled (get an IPv6 address) for IPv6 like any other device on the network.
For the router to “act” as an IPv6 router it must be enabled with the ipv6-unicast routing command.
This enables the router to:
  Send Router Advertisement messages
All-routers on this link (Assigned)

## Slide 176
Enabling IPv6 Routing
R1(config)# ipv6 unicast-routing
R1# show ipv6 interface fastethernet 0/0
Joined group address(es):
FF02::2
A router’s interfaces can be enabled (get an IPv6 address) for IPv6 like any other device on the network.
For the router to “act” as an IPv6 router it must be enabled with the ipv6-unicast routing command.
This enables the router to:
  Send Router Advertisement messages
  Enable the forwarding of IPv6 packets.
All-routers on this link (Assigned)

## Slide 177
Enabling IPv6 Routing
R1(config)# ipv6 unicast-routing
R1# show ipv6 interface fastethernet 0/0
Joined group address(es):
FF02::2
A router’s interfaces can be enabled (get an IPv6 address) for IPv6 like any other device on the network.
For the router to “act” as an IPv6 router it must be enabled with the ipv6-unicast routing command.
This enables the router to:
  Send Router Advertisement messages
  Enable the forwarding of IPv6 packets.
  Participate in IPv6 routing protocols: RIPng, EIGRP for IPv6, OSPFv3
All-routers on this link (Assigned)

## Slide 178
NDP Router Solicitation
ipv6 unicast-routing
1
RouterA
DHCPv6 Server
Stateless Addressing
2
RA(config)# ipv6 unicast-routing
NDP Router Advertisement
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Or
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Or
“I can’t help you. Ask a DHCPv6 server for all your information.”

## Slide 179
IPv6 Addressing
Multicast Addresses
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80

## Slide 180
Similar to IPv4 Multicast
Similar to IPv4 ALL SPF Routers 224.0.0.5

## Slide 181
IPv6 Addressing
Multicast Addresses
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80

## Slide 182
NIC: I will listen for my MAC address
IP: I listen for my IP addresses (Global and Link-local)
Global Unicast Address:
Link-local Unicast Address:
MAC Unicast Address:
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FE80::1111:2222:3333:4444
00-19-D2-8C-E0-4C
PC-2
Devices list for their unicast addresses.
MAC
IP: Global or Link-local

## Slide 183
NIC: I will listen for my MAC address
IP: I listen for my IP addresses (Global and Link-local)
Global Unicast Address:
Link-local Unicast Address:
MAC Unicast Address:
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FE80::1111:2222:3333:4444
00-19-D2-8C-E0-4C
PC-2
Devices list for their unicast addresses.
Devices also listen for their multicast addresses…
MAC
IP: Global or Link-local

## Slide 184
Solicited-node multicast addresses for PC2
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Link-local Unicast Address:
MAC Unicast Address:
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FE80::1111:2222:3333:4444
00-19-D2-8C-E0-4C
PC-2

## Slide 185
Solicited-node multicast addresses for PC2
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Solicited Node (Global):
Link-local Unicast Address:
MAC Unicast Address:
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
FE80::1111:2222:3333:4444
00-19-D2-8C-E0-4C
PC-2

## Slide 186
Solicited-node multicast addresses for PC2
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Solicited Node (Global):
Link-local Unicast Address:
Solicited Node (Link-local):
MAC Unicast Address:
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
FE80::1111:2222:3333:4444
FF02::1:FF33:4444
00-19-D2-8C-E0-4C
PC-2

## Slide 187
Solicited-node multicast addresses for PC2
NIC: I will also listen for my MAC multicast addresses
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Solicited Node (Global):
Link-local Unicast Address:
Solicited Node (Link-local):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
FE80::1111:2222:3333:4444
FF02::1:FF33:4444
00-19-D2-8C-E0-4C
33-33-FF-00-02-00
33-33-FF-33-44-44
PC-2

## Slide 188
Solicited-node multicast addresses for PC2
NIC: I will also listen for my MAC multicast addresses
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Solicited Node (Global):
Link-local Unicast Address:
Solicited Node (Link-local):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
FE80::1111:2222:3333:4444
FF02::1:FF33:4444
00-19-D2-8C-E0-4C
33-33-FF-00-02-00
33-33-FF-33-44-44
PC-2
Broadcasts

## Slide 189
Solicited-node multicast address
Interface ID
Global Routing Prefix
Subnet ID
104 bits
Unicast/Anycast Address
Devices create a solicited node multicast address for their unicast (and anycast) addresses including:
  Global Unicast Address (Unique Local also)
  Link-local Address

## Slide 190
Solicited-node multicast address
Interface ID
FF02
24 bits
0000
0000
0000
0000
0001
FF
Global Routing Prefix
Subnet ID
104 bits
Unicast/Anycast Address
Solicited-Node Multicast Address
104 bits
FF02:0:0:0:0:1:FF00::/104
Uses the prefix:FF02:0:0:0:0:1:FF00::/104

## Slide 191
Solicited-node multicast address
Interface ID
FF02
24 bits
0000
0000
0000
0000
0001
FF
Global Routing Prefix
Subnet ID
104 bits
24 bits
Unicast/Anycast Address
Solicited-Node Multicast Address
Copy
104 bits
FF02:0:0:0:0:1:FF00::/104
Uses the prefix:FF02:0:0:0:0:1:FF00::/104
+ last 24 bits of Global or Link-local unicast address

## Slide 192
Used as a destination address when don’t know the unicast address.
  Address Resolution (“ARP”) and Duplicate Address Detection (“Gratuitous ARP”)
Solicited-node multicast address
Interface ID
FF02
24 bits
0000
0000
0000
0000
0001
FF
Global Routing Prefix
Subnet ID
104 bits
24 bits
Unicast/Anycast Address
Solicited-Node Multicast Address
Copy
104 bits
FF02:0:0:0:0:1:FF00::/104

## Slide 193
Used as a destination address when don’t know the unicast address.
  Address Resolution (“ARP”) and Duplicate Address Detection (“Gratuitous ARP”)
Same intent as a broadcast but more efficient.
Solicited-node multicast address
Interface ID
FF02
24 bits
0000
0000
0000
0000
0001
FF
Global Routing Prefix
Subnet ID
104 bits
24 bits
Unicast/Anycast Address
Solicited-Node Multicast Address
Copy
104 bits
FF02:0:0:0:0:1:FF00::/104

## Slide 194
Used as a destination address when don’t know the unicast address.
  Address Resolution (“ARP”) and Duplicate Address Detection (“Gratuitous ARP”)
Same intent as a broadcast but more efficient.
Devices process packets with their solicited node multicast address as the destination address: IP and MAC.
Solicited-node multicast address
Interface ID
FF02
24 bits
0000
0000
0000
0000
0001
FF
Global Routing Prefix
Subnet ID
104 bits
24 bits
Unicast/Anycast Address
Solicited-Node Multicast Address
Copy
104 bits
FF02:0:0:0:0:1:FF00::/104

## Slide 195
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
Solicited-node multicast address for Global Unicast Address
Last 24 bits of Global Unicast Address

## Slide 196
R1# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::203:6BFF:FEE9:D480
Global unicast address(es):
2001:DB8:AAAA:1::1, subnet is 2001:DB8:AAAA:1::/64
Joined group address(es):
FF02::1
FF02::2
FF02::1:FF00:1
FF02::1:FFE9:D480
<output omitted for brevity>
Solicited-node multicast address for Link-local Unicast Address
Last 24 bits of Link-Local Unicast Address

## Slide 197
Router(config)# interface fastethenet 0/0
Router(config-if)# ipv6 address 2001:db8:cafe:1::/64 eui-64
Router# show ipv6 interface fastethernet 0/0
FastEthernet0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::21B:CFF:FEC2:82D8
No Virtual link-local address(es):
Global unicast address(es):
2001:DB8:CAFE:1:21B:CFF:FEC2:82D8, subnet is 2001:DB8:CAFE:1::/64 [EUI]
Joined group address(es):
FF02::1
FF02::2
FF02::1:FFC2:82D8
NOTE: If the Global and Link-local addresses used EUI-64 the last 24 bits would be the same and there would only be one solicited node address.
Solicited-node multicast address for Global and Link-local unicast addresses
Last 24 bits of both Unicast Addresses

## Slide 198
Solicited-node multicast addresses for PC2
NIC: I will also listen for my MAC multicast addresses
IP: I will also listen for my IP multicast addresses (Global and Link-local)
Global Unicast Address:
Solicited Node (Global):
Link-local Unicast Address:
Solicited Node (Link-local):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
FE80::1111:2222:3333:4444
FF02::1:FF33:4444
00-19-D2-8C-E0-4C
33-33-FF-00-02-00
33-33-FF-33-44-44
PC-2

## Slide 199
Interface ID
Global Routing Prefix
104 bits
PC2’s Global Unicast Address
Subnet ID
2001:0DB8:AAAA
0001
0000:0000:00
00:0200

## Slide 200
Interface ID
FF02
0000
0000
0000
0000
0001
FF
Global Routing Prefix
104 bits
24 bits
PC2’s Global Unicast Address
PC2’s IPv6 Solicited-Node Multicast Address
Copy
Subnet ID
2001:0DB8:AAAA
0001
0000:0000:00
00:0200
00:0200

## Slide 201
Interface ID
FF02
0000
0000
0000
0000
0001
FF
Global Routing Prefix
104 bits
24 bits
PC2’s Global Unicast Address
PC2’s IPv6 Solicited-Node Multicast Address
Copy
PC2’s mapped solicited-node Ethernet multicast address : 33-33-FF-00-02-00
Subnet ID
2001:0DB8:AAAA
0001
0000:0000:00
00:0200
00:0200
FF-00-02-00
Copy
33-33
Solicited-node Multicast address mapped to Ethernet destination MAC address

## Slide 202
At Layer 2 and 3 I am listening for a lot of addresses.
Global Unicast Address:
Solicited Node (Global):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
33-33-FF-00-02-00
PC-2
Why Solicited Node Addresses?

## Slide 203
At Layer 2 and 3 I am listening for a lot of addresses.
Global Unicast Address:
Solicited Node (Global):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
33-33-FF-00-02-00
PC-2
Why Solicited Node Addresses?
Broadcasts are sent to all devices.

## Slide 204
At Layer 2 and 3 I am listening for a lot of addresses.
Global Unicast Address:
Solicited Node (Global):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
33-33-FF-00-02-00
PC-2
Why Solicited Node Addresses?
Broadcasts are sent to all devices.
Devices must process all broadcast at least to layer 3.

## Slide 205
At Layer 2 and 3 I am listening for a lot of addresses.
Global Unicast Address:
Solicited Node (Global):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
33-33-FF-00-02-00
PC-2
Why Solicited Node Addresses?
Broadcasts are sent to all devices.
Devices must process all broadcast at least to layer 3.
Solicited Node Multicasts are only processed by those devices with the matching last 24 bits (usually one device).

## Slide 206
At Layer 2 and 3 I am listening for a lot of addresses.
Global Unicast Address:
Solicited Node (Global):
MAC Unicast Address:
Solicited Node (MAC):
2001:0DB8:AAAA:0001:0000:0000:0000:0200
FF02::1:FF00:200
33-33-FF-00-02-00
PC-2
Why Solicited Node Addresses?
Broadcasts are sent to all devices.
Devices must process all broadcast at least to layer 3.
Solicited Node Multicasts are only processed by those devices with the matching last 24 bits (usually one device).
If I know the IPv6 address but not the MAC address I can send it to a solicited node addresses instead of a broadcast to everyone…

## Slide 207
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00

## Slide 208
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
IPv6 Header
I know the target IPv6 Address…

## Slide 209
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
Destination IPv6
FF02::1FF00:200
Source IPv6
2002:0DB8:AAAA:0001::0100
IPv6 Header
So, I can create a Solicited Node Multicast Address…

## Slide 210
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
Source MAC
00-12-34-56-78-9A
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
Destination IPv6
FF02::1FF00:200
Source IPv6
2002:0DB8:AAAA:0001::0100
Dest. MAC
33-33-FF-00-02-00
IPv6 Header
So, I can create a Solicited Node MAC Address…

## Slide 211
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
NIC: That’s one of my solicited node MAC addresses.
IPv6: That’s one of my solicited node addresses.
Source MAC
00-12-34-56-78-9A
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
Destination IPv6
FF02::1FF00:200
Source IPv6
2002:0DB8:AAAA:0001::0100
Dest. MAC
33-33-FF-00-02-00
IPv6 Header

## Slide 212
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
NIC: That’s one of my solicited node MAC addresses.
IPv6: That’s one of my solicited node addresses.
Source MAC
00-12-34-56-78-9A
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
Destination IPv6
FF02::1FF00:200
Source IPv6
2002:0DB8:AAAA:0001::0100
Dest. MAC
33-33-FF-00-02-00
IPv6 Header
Possible that multiple devices may have the same last 24 bits in their IPv6 address but only those devices would have to process up to the target.

## Slide 213
PC-1
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Whoever has 2001:0DB8:AAAA:1::0200 send me your Ethernet MAC address”
Address Resolution
PC-2
2001:0DB8:AAAA:1::0200
FF02::1:FF00:200
2001:0DB8:AAAA:1::0100
MAC: 00-19-D2-8C-E0-4C
33-33-FF-00-02-00
NIC: That’s one of my solicited node MAC addresses.
IPv6: That’s one of my solicited node addresses.
Source MAC
00-12-34-56-78-9A
Ethernet
ICMPv6
Target IPv6
2002:0DB8:AAAA:0001::0200
Destination IPv6
FF02::1FF00:200
Source IPv6
2002:0DB8:AAAA:0001::0100
Dest. MAC
33-33-FF-00-02-00
IPv6 Header
PC-2 replies with it’s MAC address (Neighbor Advertisement Message)
More in ICMPv6 presentation!

## Slide 214
Use of solicited-node multicasts with addressing resolution and DAD
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Before I use this address is anyone else on this link using this link-local address:
FE80::50A5:8A35:A5BB:66E1?”
Duplicate Address Detection (DAD)
NDP Neighbor Solicitation Message
Destination: Solicited-node Multicast
“Who ever has the IPv6 address 2001:0DB8:AAAA:0001::0200 please send me your Ethernet MAC address”
Address Resolution
Similar to ARP in IPv4
Similar to gratuitous ARP in IPv4

## Slide 215
Quick look at the routing table…

## Slide 216
R1# show ip route
Codes: C - connected, S - static, R - RIP, M - mobile,
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
<output omitted>
Gateway of last resort is not set
R1# show ipv6 route
IPv6 Routing Table - 8 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B – BGP
<output omitted>
<output omitted>
R1#

## Slide 217
R1# show ipv6 route connected
IPv6 Routing Table - 11 entries
Codes: C - Connected, L - Local, S - Static, R - RIP,
<output omitted>
C 2001:DB8:CAFE:1::/64 [0/0]
via ::, FastEthernet0/0
C 2001:DB8:CAFE:A001::/64 [0/0]
via ::, Serial0/0/0
R1#
“connected”
Directly connected networks

## Slide 218
R1# show ipv6 route local
Codes: C - Connected, L - Local, S - Static, R – RIP
<output omitted>
L 2001:DB8:CAFE:1::1/128 [0/0]
via ::, FastEthernet0/0
L 2001:DB8:CAFE:A001::1/128 [0/0]
via ::, Serial0/0/0
L FE80::/10 [0/0]
via ::, Null0
L FF00::/8 [0/0]
via ::, Null0
R1#
“local”
Local Host NOT Link-local

## Slide 219
R1# show ipv6 route local
Codes: C - Connected, L - Local, S - Static, R – RIP
<output omitted>
L 2001:DB8:CAFE:1::1/128 [0/0]
via ::, FastEthernet0/0
L 2001:DB8:CAFE:A001::1/128 [0/0]
via ::, Serial0/0/0
L FE80::/10 [0/0]
via ::, Null0
L FF00::/8 [0/0]
via ::, Null0
R1#
“local”
Local Host NOT Link-local
Allows the router to know when a packet is addressed to itself.

## Slide 220
R1# show ipv6 route local
Codes: C - Connected, L - Local, S - Static, R – RIP
<output omitted>
L 2001:DB8:CAFE:1::1/128 [0/0]
via ::, FastEthernet0/0
L 2001:DB8:CAFE:A001::1/128 [0/0]
via ::, Serial0/0/0
L FE80::/10 [0/0]
via ::, Null0
L FF00::/8 [0/0]
via ::, Null0
R1#
“local”
Local Host NOT Link-local
Allows the router to know when a packet is addressed to itself.
FE80::/10 and FF00::8 -> Null0
These are non-routable addresses.

## Slide 221
R1# show ipv6 route local
Codes: C - Connected, L - Local, S - Static, R – RIP
<output omitted>
L 2001:DB8:CAFE:1::1/128 [0/0]
via ::, FastEthernet0/0
L 2001:DB8:CAFE:A001::1/128 [0/0]
via ::, Serial0/0/0
L FE80::/10 [0/0]
via ::, Null0
L FF00::/8 [0/0]
via ::, Null0
R1#
“local”
Local Host NOT Link-local
Allows the router to know when a packet is addressed to itself.
FE80::/10 and FF00::8 -> Null0
These are non-routable addresses.
These packets will be dropped.

## Slide 222
R1# show ipv6 route local
Codes: C - Connected, L - Local, S - Static, R – RIP
<output omitted>
L 2001:DB8:CAFE:1::1/128 [0/0]
via ::, FastEthernet0/0
L 2001:DB8:CAFE:A001::1/128 [0/0]
via ::, Serial0/0/0
L FE80::/10 [0/0]
via ::, Null0
L FF00::/8 [0/0]
via ::, Null0
R1#
“local”
Local Host NOT Link-local
Allows the router to know when a packet is addressed to itself.
FE80::/10 and FF00::8 -> Null0
These are non-routable addresses.
These packets will be dropped.
Why you must give exit interface when pinging link-local address.

## Slide 223
To summarize…

## Slide 224
IPv6 Addressing
IPv6 Address Types
Multicast
Unicast
Anycast
Assigned
Solicited Node
Global Unicast
Unspecified
Loopback
Embedded IPv4
Link-Local
Unique Local
FF00::/8
FF02::1:FF00:0000/104
::/128
::1/128
2000::/3
3FFF::/3
FE80::/10
FEBF::/10
FC00::/7
FDFF::/7
::/80
Note: There are no broadcast addresses in IPv6

## Slide 225
Global Unicast
Global Unicast Addresses
IPv6 Unnumbered
Stateless Autoconfiguration
Static
EUI-64
Manual
IPv6 Address
Dynamic
DHCPv6

## Slide 226: For more information
Web site: www.cabrillo.edu/~rgraziani
Username = cisco
Password = perlman
Email: graziani@cabrillo.edu

## Slide 227: For more information
Web site: www.cabrillo.edu/~rgraziani
Username = cisco
Password = perlman
Email: graziani@cabrillo.edu
IPv6 Fundamentals: A Straightforward Approach to Understanding IPv6
By Rick Graziani
Shameless plug!

## Slide 228
Thank you for hanging in there!
Questions?