## Slide 1: Lecture 4: Application Layer

## Slide 2: 15.1 Application, Presentation, and Session

## Slide 3: Application, Presentation, and Session Application Layer
The upper three layers of the OSI model (application, presentation, and session) define functions of the TCP/IP application layer.
The application layer provides the interface between the applications used to communicate, and the underlying network over which messages are transmitted.
Some of the most widely known application layer protocols include HTTP, FTP, TFTP, IMAP and DNS.
Notes:     What are some protocols at the application layer of the TCP/IP model?
    Why is the application layer of the TCP/IP model considered to be closest to the end user?
    Why do you think the TCP/IP model combines the application, presentation and session layers into one layer?

## Slide 4: Application, Presentation, and Session Presentation and Session Layer
The presentation layer has three primary functions:
    Formatting, or presenting, data at the source device into a compatible format for receipt by the destination device
    Compressing data in a way that can be decompressed by the destination device
    Encrypting data for transmission and decrypting data upon receipt
The session layer functions:
      It creates and maintains dialogs between source and destination applications.
      It handles the exchange of information to initiate dialogs, keep them active, and to restart sessions that are disrupted or idle for a long period of time.

## Slide 5: Application, Presentation, and Session TCP/IP Application Layer Protocols
The TCP/IP application protocols specify the format and control information necessary for many common internet communication functions.
Application layer protocols are used by both the source and destination devices during a communication session.
For the communications to be successful, the application layer protocols that are implemented on the source and destination host must be compatible.
Name System
DNS - Domain Name System (or Service)
TCP, UDP client 53
Translates domain names, such as cisco.com, into IP addresses.
Host Config
DHCP - Dynamic Host Configuration Protocol
UDP client 68, server 67
Dynamically assigns IP addresses to be re-used when no longer needed
Web
HTTP - Hypertext Transfer Protocol
TCP 80, 8080
A set of rules for exchanging text, graphic images, sound, video, and other multimedia files on the World Wide Web

## Slide 6: 15.2 Peer-to-Peer

## Slide 7: Peer-to-Peer Client-Server Model
Client and server processes are considered to be in the application layer.
In the client/server model, the device requesting the information is called a client and the device responding to the request is called a server.
Application layer protocols describe the format of the requests and responses between clients and servers.

## Slide 8: Peer-to-Peer Peer-to-Peer Networks
In a peer-to-peer (P2P) network, two or more computers are connected via a network and can share resources (such as printers and files) without having a dedicated server.
Every connected end device (known as a peer) can function as both a server and a client.
One computer might assume the role of server for one transaction while simultaneously serving as a client for another. The roles of client and server are set on a per request basis.
Notes:     What are some advantages/disadvantages of using a peer-to-peer network?
    Has anyone ever used a peer-to-peer network?
    Is anyone familiar with or heard about any of the peer-to-peer applications (BitTorrent, Direct Connect, eDonkey etc.)?

## Slide 9: Peer-to-Peer Peer-to-Peer Applications
A P2P application allows a device to act as both a client and a server within the same communication.
Some P2P applications use a hybrid system where each peer accesses an index server to get the location of a resource stored on another peer.

## Slide 10: Peer-to-Peer Common P2P Applications
With P2P applications, each computer in the network that is running the application can act as a client or a server for the other computers in the network that are also running the application.
Common P2P networks include the following:
    BitTorrent
    Gnutella
    Direct Connect
    eDonkey (eMule)
    Freenet
    Blockchain / Crypto (P2P Modern)

## Slide 11: P2P Comparison
Network | Centralization | Status | Used for
BitTorrent | Decentralized | ✅ Active | Large files
Gnutella | Fully decentralized | ⚠️ Reduced | File search
eDonkey/eMule | Semi-centralized | ⚠️ Reduced | Large files
Napster | Centralized | ❌ Shut down | Music
Bitcoin | Fully decentralized | ✅ Active | Transactions
Old Skype | Decentralized | ❌ Changed | Voice/Video

## Slide 12: P2P Advantages vs Disadvantages
Advantages | Disadvantages
✅ Not dependent on a central server | ❌ Difficult to control/moderate
✅ More peers → faster speeds | ❌ Weaker security
✅ Resistant to censorship/shutdown | ❌ Can be used illegally
✅ Low infrastructure costs | ❌ Inconsistent speed
✅ Automatically scalable | ❌ Requires special software

## Slide 13: 15.3 Web and Email Protocols

## Slide 14: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language
When a web address or Uniform Resource Locator (URL) is typed into a web browser, the web browser establishes a connection to the web service. The web service is running on the server that is using the HTTP protocol.
To better understand how the web browser and web server interact, examine how a web page is opened in a browser.
Step 1
The browser interprets the three parts of the URL:
http (the protocol or scheme)
www.cisco.com (the server name)
index.html (the specific filename requested)
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.1 – Hypertext Transfer Protocol and Hypertext Markup Language

## Slide 15: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language (Cont.)
Step 2
The browser then checks with a name server to convert www.cisco.com into a numeric IP address, which it uses to connect to the server.
The client initiates an HTTP request to a server by sending a GET request to the server and asks for the index.html file.
Step 3
In response to the request, the server sends the HTML code for this web page to the browser.

## Slide 16: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language (Cont.)
Step 4
The browser deciphers the HTML code and formats the page for the browser window.

## Slide 17: Web and Email Protocols HTTP and HTTPS
HTTP is a request/response protocol that specifies the message types used for that communication.
The three common message types are GET, POST, and PUT:
    GET - This is a client request for data. A client (web browser) sends the GET message to the web server to request HTML pages.
    POST - This uploads data files to the web server, such as form data.
    PUT - This uploads resources or content to the web server, such as an image.
Note: HTTP is not a secure protocol. For secure communications sent across the internet, HTTPS should be used.

## Slide 18: Web and Email Protocols Email Protocols
Email is a store-and-forward method of sending, storing, and retrieving electronic messages across a network. Email messages are stored in databases on mail servers. Email clients communicate with mail servers to send and receive email.
The email protocols used for operation are:
    Simple Mail Transfer Protocol (SMTP) – used to send mail.
    Post Office Protocol (POP) & IMAP – used for clients to receive mail.
Notes:     Why is HTTPS recommended over HTTP on websites such as banks or online stores?
    What are the three common HTTP message types?
    What is the difference between POP3 and IMAP?

## Slide 19: Web and Email Protocols SMTP, POP and IMAP
When a client sends email, the client SMTP process connects with a server SMTP process on well-known port 25.
After the connection is made, the client attempts to send the email to the server across the connection.
When the server receives the message, it either places the message in a local account, if the recipient is local, or forwards the message to another mail server for delivery.
The destination email server may not be online or may be busy. If so, SMTP spools messages to be sent at a later time.
Note: SMTP message formats require a message header (recipient email address & sender email address) and a message body.

## Slide 20: Web and Email Protocols SMTP, POP and IMAP (Cont.)
POP is used by an application to retrieve mail from a mail server. When mail is downloaded from the server to the client using POP the messages are then deleted on the server.
  The server starts the POP service by passively listening on TCP port 110 for client connection requests.
  When a client wants to make use of the service, it sends a request to establish a TCP connection with the server.
  When the connection is established, the POP server sends a greeting.
  The client and POP server then exchange commands and responses until the connection is closed or aborted.
Note: Since POP does not store messages, it is not recommended for small businesses that need a centralized backup solution.

## Slide 21: Web and Email Protocols SMTP, POP and IMAP (Cont.)
IMAP is another protocol that describes a method to retrieve email messages.
Unlike POP, when a user connects to an IMAP server, copies of the messages are downloaded to the client application. The original messages are kept on the server until manually deleted.
When a user decides to delete a message, the server synchronizes that action and deletes the message from the server.

## Slide 22: 15.4 IP Addressing Services

## Slide 23: IP Addressing Services Domain Name Service
Domain names were created to convert the numeric IP addresses into a simple, recognizable name.
Fully-qualified domain names (FQDNs), such as http://www.cisco.com, are much easier for people to remember than 198.133.219.25.
The DNS protocol defines an automated service that matches resource names with the required numeric network address. It includes the format for queries, responses, and data.

## Slide 24: IP Addressing Services DNS Message Format
The DNS server stores different types of resource records that are used to resolve names. These records contain the name, address, and type of record.
Some of these record types are as follows:
    A - An end device IPv4 address
    NS - An authoritative name server
    AAAA - An end device IPv6 address (pronounced quad-A)
    MX - A mail exchange record
When a client makes a query, the server DNS process first looks at its own records to resolve the name. If it is unable to resolve the name by using its stored records, it contacts other servers to resolve the name.
After a match is found and returned to the original requesting server, the server temporarily stores the numbered address in the event that the same name is requested again.

## Slide 25: IP Addressing Services DNS Message Format (Cont.)
DNS uses the same message format between servers, consisting of a question, answer, authority, and additional information for all types of client queries and server responses, error messages, and transfer of resource record information.
DNS message section | Description
Question | The question for the name server
Answer | Resource Records answering the question
Authority | Resource Records pointing toward an authority
Additional | Resource Records holding additional information

## Slide 26: IP Addressing Services DNS Hierarchy
DNS uses a hierarchical system to create a database to provide name resolution.
Each DNS server maintains a specific database file and is only responsible for managing name-to-IP mappings for that small portion of the entire DNS structure.
When a DNS server receives a request for a name translation that is not within its DNS zone, the DNS server forwards the request to another DNS server within the proper zone for translation.
Examples of top-level domains:
    .com - a business or industry
    .org - a non-profit organization
    .au - Australia

## Slide 27: IP Addressing Services The nslookup Command
Nslookup is a computer operating system utility that allows a user to manually query the DNS servers configured on the device to resolve a given host name.
This utility can also be used to troubleshoot name resolution issues and to verify the current status of the name servers.
When the nslookup command is issued, the default DNS server configured for your host is displayed.
The name of a host or domain can be entered at the nslookup prompt.

## Slide 28: IP Addressing Services Dynamic Host Configuration Protocol
The Dynamic Host Configuration Protocol (DHCP) for IPv4 service automates the assignment of IPv4 addresses, subnet masks, gateways, and other IPv4 networking parameters.
DHCP is considered dynamic addressing compared to static addressing. Static addressing is manually entering IP address information.
When a host connects to the network, the DHCP server is contacted, and an address is requested. The DHCP server chooses an address from a configured range of addresses called a pool and assigns (leases) it to the host.
Many networks use both DHCP and static addressing. DHCP is used for general purpose hosts, such as end user devices. Static addressing is used for network devices, such as gateway routers, switches, servers, and printers.
Note: DHCP for IPv6 (DHCPv6) provides similar services for IPv6 clients. However, DHCPv6 does not provide a default gateway address. This can only be obtained dynamically from the Router Advertisement message of the router.

## Slide 29: IP Addressing Services DHCP Operation
The DHCP Process:
    When an IPv4, DHCP-configured device boots up or connects to the network, the client broadcasts a DHCP discover (DHCPDISCOVER) message to identify any available DHCP servers on the network.
    A DHCP server replies with a DHCP offer (DHCPOFFER) message, which offers a lease to the client. (If a client receives more than one offer due to multiple DHCP servers on the network, it must choose one.)
    The client sends a DHCP request (DHCPREQUEST) message that identifies the explicit server and lease offer that the client is accepting.
    The server then returns a DHCP acknowledgment (DHCPACK) message that acknowledges to the client that the lease has been finalized.
    If the offer is no longer valid, then the selected server responds with a DHCP negative acknowledgment (DHCPNAK) message and the process must begin with a new DHCPDISCOVER message.
Note: DHCPv6 has a set of messages that is similar to those for DHCPv4. The DHCPv6 messages are SOLICIT, ADVERTISE, INFORMATION REQUEST, and REPLY.

## Slide 30: IP Addressing Services Practice – Observe DNS Resolution
# Simple
nslookup google.com
# Specific DNS server interrogation
nslookup google.com 8.8.8.8
# MX (mail) record listing
nslookup -type=MX gmail.com
# NS records listing (name servers)
nslookup -type=NS google.com
# Reverse DNS (IP → name)
nslookup 8.8.8.8

## Slide 31: IP Addressing Services Practice – Observe DNS Resolution
Type | Significance | Use example
A | IPv4 address | nslookup -type=A site.com
AAAA | IPv6 address | nslookup -type=AAAA site.com
MX | Mail server | nslookup -type=MX gmail.com
NS | Nameserver | nslookup -type=NS site.com
TXT | Text (SPF, DKIM) | nslookup -type=TXT site.com
SOA | Start of Authority | nslookup -type=SOA site.com
CNAME | Alias / redirect | nslookup -type=CNAME www.site.com
PTR | Reverse DNS | nslookup IP_address

## Slide 32: IP Addressing Services Practice – Observe DNS Resolution
Funny fact: Easter egg – facebook.com
>nslookup www.facebook.com
Server: uranus.intra.net.ase.ro
Address: 192.168.3.10
Non-authoritative answer:
Name: star-mini.c10r.facebook.com
Addresses: 2a03:2880:f123:83:face:b00c:0:25de
185.60.218.35
Aliases: www.facebook.com
>nslookup 74.125.206.27
Server: uranus.intra.net.ase.ro
Address: 192.168.3.10
Name: wk-in-f27.1e100.net
Address: 74.125.206.27
gmail.com
└── MX → gmail-smtp-in.l.google.com
└── A → 74.125.206.27
└── PTR → wk-in-f27.1e100.net (Google!)

## Slide 33: IP Addressing Services Practice – Observe DNS Resolution
SOA=Start of Authority – an “id card” of the DNS zone
nslookup -type=SOA google.com
Server: UnKnown
Address: 100.100.1.1
Non-authoritative answer:
google.com
primary name server = ns1.google.com
responsible mail addr = dns-admin.google.com
serial = 879543655
refresh = 900 (15 mins)
retry = 900 (15 mins)
expire = 1800 (30 mins)
default TTL = 60 (1 min)
primary name server = master DNS
google server
dns-admin.google.com = DNS admin
email
serial – DNS zone version
refresh – how often the check is done
relative to primary server
retry – if primary server is not responding,
how often is done the retry
expire – the period after the information is
considered expired, if the primary server
doesn’t respond
default TTL – how much time other servers
can keep the information in cache

## Slide 34: 15.5 File Sharing Services

## Slide 35: File Sharing Services File Transfer Protocol
FTP was developed to allow for data transfers between a client and a server. An FTP client is an application which runs on a computer that is being used to push and pull data from an FTP server.
Step 1 - The client establishes the first connection to the server for control traffic using TCP port 21. The traffic consists of client commands and server replies.
Step 2 - The client establishes the second connection to the server for the actual data transfer using TCP port 20. This connection is created every time there is data to be transferred.
Step 3 - The data transfer can happen in either direction. The client can download (pull) data from the server, or the client can upload (push) data to the server.

## Slide 36: File Sharing Services Server Message Block
The Server Message Block (SMB) is a client/server, request-response file sharing protocol. Servers can make their own resources available to clients on the network.
Three functions of SMB messages:
    Start, authenticate, and terminate sessions
    Control file and printer access
    Allow an application to send or receive messages to or from another device
Unlike the file sharing supported by FTP, clients establish a long-term connection to servers. After the connection is established, the user of the client can access the resources on the server as though the resource is local to the client host.
Notes:     Why does a client establish two connections to an FTP server?
    What are the differences between FTP and Server Message Block (SMB)?

## Slide 37: Module 15 : Application Layer New Terms and Commands
Application Layer Presentation Layer Session Layer Client-server model Peer-to-peer Uniform Resource Locator (URL) Uniform Resource Identifiers (URI) HTTP/HTTPS GET POST PUT SMTP POP | IMAP Domain Name Service (DNS) Fully-Qualified Domain Names (FQDNs) nslookup Dynamic Host Configuration Protocol (DHCP) DHCPDISCOVER DHCPOFFER DHCPREQUEST DHCPACK File Transfer Protocol (FTP) Server Message Block (SMB)