## Slide 1
COURSE LECTURE 13
AI Applications in
Networking
From Automation to Autonomous Networks — The Future Is Now

## Slide 2
Course Agenda
01
AI-Driven Network Management
Intent-based, self-optimizing networks
02
Predictive Analytics & AIOps
Anomaly detection, root cause analysis
03
AI in Cybersecurity
Threat detection, zero-trust architectures
04
Network Slicing & 5G/6G
Intelligent resource allocation
05
SD-WAN & AI Optimization
Autonomous traffic engineering
06
Emerging Trends
LLMs for networking, future outlook

## Slide 3
01
AI-Driven Network Management
Intent-Based
Networking (IBN)
AI translates high-level business intent into network configurations automatically.
Examples: Cisco DNA Center, Juniper Apstra.
Self-Healing
Networks
ML models detect faults and reroute traffic in real-time — reducing MTTR from hours to seconds.
Closed-Loop
Automation
Continuous feedback loops: monitor → analyze → act.
Zero human intervention for routine tasks.
60%
reduction in
ops costs (Gartner)

## Slide 4
02 AIOps & Predictive Analytics
What is AIOps?
AIOps (AI for IT Operations) applies ML and big data to automate and enhance network operations — enabling real-time insights at scale.
Anomaly Detection
Detect unusual traffic patterns before they become outages
Capacity Forecasting
Predict bandwidth needs weeks in advance
Root Cause Analysis
Correlate events across thousands of devices instantly
Performance Baselining
Dynamic thresholds adapt to changing network behavior
Key Platforms
▸ Cisco ThousandEyes — end-to-end visibility
▸ Juniper Mist AI (Marvis agent)— wireless & wired AIOps
▸ Splunk ITSI (IT Service Intelligence) — event correlation at scale
▸ Datadog NPM (Network Performance Monitoring) — cloud-native network monitoring

## Slide 5
03
AI in Cybersecurity
2,200+
cyber attacks per day
globally (2025)
Behavioral Analytics (UEBA - User and Entity Behavior Analytics)
ML baselines normal user/device behavior; flags deviations instantly.
AI-Powered SIEM (Security Information and Event Management)
Automated threat correlation reduces false positives by 90%.
Zero Trust + AI
Continuous authentication; AI scores every access request in real-time.
Deception Technology – proactive cybersecurity strategy
AI-generated honeypots/honeytokens to trap attackers with minimal false positives.

## Slide 6
04 Network Slicing & 5G / 6G
AI enables dynamic, on-demand allocation of virtual network slices tailored to specific applications — a core requirement for 5G/6G deployments.
eMBB
Enhanced Mobile Broadband – ultra high speed
AI manages spectrum allocation for AR/VR, 8K streaming.
Very high transfer speed (100 Mbps - >1 Gbps)
User experience – instant video streaming 4k/8k resolution
AI Role
Dynamic spectrum
reallocation
URLLC
Ultra-Reliable Low Latency (instant reaction, 99.999% reliability )
AI guarantees <1ms latency for autonomous vehicles & surgery.
Latency drops from 30-50 ms in 4G to 1-5 ms in 5G
Safety: extremely reliable connection
AI Role
Predictive
scheduling
mMTC
Massive Machine-Type Comm. (large scale IoT)
AI orchestrates millions of IoT connections simultaneously.
High density communication – up to 1 million devices per square km
Energy efficiency: battery life up to 10 years
AI Role
Cluster-based
device grouping

## Slide 7
05
SD-WAN & AI Traffic Optimization
Intelligent Path
Selection
RL (Reinforcement Learning) agents continuously evaluate MPLS, broadband, and LTE (Long-Term Evolution) paths, choosing the optimal route per-application in real-time.
Application-Aware
QoS
Deep packet inspection + ML classifies 3,000+ apps and enforces dynamic priority policies automatically.
Predictive
Failover
AI predicts link degradation 30–60 seconds before failure and pre-routes traffic — zero dropped calls.
WAN
Optimization
Deduplication, caching, and compression guided by usage patterns, reducing bandwidth consumption up to 70%.

## Slide 8
06 Large Language Models in Networking
LLMs are transforming how engineers interact with and troubleshoot networks — turning natural language into config and insights.
Natural Language to Config
"Block all traffic from AS 12345" → Auto-generates ACLs, BGP policies in seconds.
Intelligent Troubleshooting
Chatbot-driven RCA (Root Cause Analysis) : describe symptoms, get a diagnosis and fix — like a NOC (Network Operations Center) engineer 24/7.
Config Audit & Compliance
LLMs parse thousands of device configs and flag policy violations automatically.
Documentation Generation
Auto-generate network runbooks and topology documentation from live data.
Tools & Products
› Cisco AI Assistant for Networking
› Juniper Marvis Virtual Network Asst.
› AWS Amazon Q for Networking
› Aruba Networking Central AI
› Nokia NetCracker Digital OSS
› Open-source: NetMind, NLP-Netconf

## Slide 9
Challenges & Considerations
Data Privacy
Training AI models on network telemetry raises compliance challenges (GDPR, NIS2 – Network and Information Security Directive 2).
Explainability
Black-box AI decisions are difficult to audit — critical in regulated industries.
Adversarial AI
Attackers can poison training data or craft evasion attacks against AI-based defenses.
Legacy Integration
Most enterprise networks have decades-old equipment incompatible with AI telemetry.
Vendor Lock-In
Proprietary AI networking stacks create long-term dependency risks.
Skill Gap
Network engineers need retraining in ML concepts and AI toolchains.

## Slide 10
The Road Ahead — Future Trends
2025–26
◆ Autonomous NOC pilots widely deployed
A NOC (Network Operations Center) is an AI-driven, intelligent hub where network monitoring, incident management, and remediation are increasingly automated through agentic AI systems, allowing minimal human intervention.
◆ LLM-native config tools standard in enterprise
2027–28
◆ AI-native 6G slicing at carrier scale
◆ Federated learning for cross-org threat sharing
2029–30
◆ Fully autonomous network lifecycle mgmt.
◆ Quantum-AI hybrid for encryption & routing
"The network of the future won't just carry data — it will think, adapt, and protect itself."

## Slide 11
Thank You
Questions & Discussion
AI Applications in Networking • Intent-Based Mgmt • AIOps • Cybersecurity • 5G Slicing • SD-WAN • LLMs