## Slide 1: Operating Systems Course #5 Filesystems
Răzvan Daniel ZOTA
Faculty of Cybernetics, Statistics and Economic Informatics
zota@ase.ro
https://zota.ase.ro/os

## Slide 2: Introduction to filesystems
What is a filesystem?
A filesystem is an integral part of an operating system, consisting of files, directories and all the information needed to access, locate (and recover, if needed) and manipulate them.

## Slide 3: File system structure – Unix/Linux

## Slide 4: File system structure – Windows
Example:

## Slide 5: The most important Linux directories
/bin | Binary (executable) files – basic system programs
/boot | System boot directory. The kernel, module links, system map (Systems.map), and boot manager reside here
/dev | Devices directory
/etc | System wide configuration scripts
/proc | Process directory. Contains information and statistics about running processes and kernel parameters
/sys | System wide device directory. Contains information and statistics about device and device names
/tmp | Temporary directory
/usr/bin | More system binaries
/usr/local/bin | Miscellaneous binaries local to the particular machine
/usr/share/doc | Documentation for installed packages
Notes: Systems.map = is a text file generated when compiling the Linux kernel that contains the kernel symbol table — basically a list of the memory addresses corresponding to each function and variable in the kernel.

## Slide 6: OSs and supported filesystems
OS | Filesystems
Windows 10/11 | NTFS, FAT32, exFAT, ReFS
Mac OS X | APFS (default), HFS+ (legacy)
Linux | Ext4, Btrfs, XFS, ZFS
NTFS (New Technology File System)- was introduced in Windows NT and at present is major file system for Windows. This is a default file system for disk partitions and the only file system that is supported for disk partitions over 32GB. The file system is quite extensible and supports many file properties, including access control, encryption etc. Each file on NTFS is stored as file descriptor in Master File Table and file content. Master file table contains all information about the file: size, allocation, name etc.
FAT12 was used for old floppy disks. FAT16 (or simply FAT) and FAT32 are widely used for flash memory cards and USB flash sticks. It is supported by mobile phones, digital cameras and other portable devices.

## Slide 7: OSs and supported filesystems
Windows 10/11: NTFS (default), FAT32, exFAT, ReFS (Server/Workstation)
macOS: APFS (default from 2017), HFS+ (legacy), exFAT, FAT32
Linux: ext4 (default), Btrfs, XFS, ZFS, tmpfs
Android/iOS: exFAT, F2FS (Flash-Friendly File System)
NTFS – default for Windows, ACL support, compression, encryption (EFS), journaling
exFAT – standard SD cards > 32GB and USB sticks, cross-platform
ReFS – Resilient File System, introduced in Windows Server 2012, checksums data integrity
APFS – Apple File System, replacing HFS+ from 2017, optimized for SSDs, snapshots native
Btrfs/ZFS – modern Linux systems with snapshots, RAID, deduplicare

## Slide 8: OSs and supported filesystems
APFS (Apple File System) – Apple's default file system since 2017 (macOS High Sierra), completely replacing HFS+. Optimized for SSDs, with native support for snapshots, per-file encryption, and copy-on-write cloning. Used on Mac, iPhone, iPad, and Apple TV. More information: https://developer.apple.com/documentation/foundation/file_system/about_apple_file_system
HFS+ (Hierarchical File System Plus) – Apple's previous file system, used until 2017. Today considered legacy – no modern Mac uses it as the default system anymore.
Ext2, Ext3, Ext4 – Linux's “native” file system. This file system is constantly being developed and improved. Ext3 is just an extension of Ext2, which uses transactional file writing operations in a “journal”. Ext4 is an extension of Ext3, providing support for optimized file allocation and extended file attributes. This file system is commonly used by most Linux installations.

## Slide 9: CDFS and UDF
CDFS (CD-ROM File System) represents a relatively simple format defined in 1988 as the CD-ROM standard. Windows implements this standard compatible with ISO 9660 in \Windows\System32\Drivers\Cdfs.sys. CDFS restrictions:
  The name (for files and directories) < 32 characters
  The tree structure for subdirectories <= 8 levels
UDF (Universal Disk Format) – a standard compatible with ISO 13346, offering support for versions 1.02 and 1.5 OSTA (Optical Storage Technology Association) defined in 1995 as a replacement format for CDFS, especially DVD-ROM.
  The names (for files and directories) <= 255 characters
  The maximum length for a path = 1023 characters
  The name of the files can be lower/upper case

## Slide 10: FAT, FAT16 and FAT32
For many years, the most popular filesystem was FAT (File Allocation Table). There are 3 types of FAT. The first one is the original FAT (FAT12), then appeared FAT16 and FAT32, improved versions for the original FAT.
The original FAT was limited from many points of view, being capable to recognize only files up to 8 characters in length.
The disk space was inefficient used, so FAT16 was built to support partitions up to 4 GB. But the space on the disk was inefficient used. For example, using a partition of 512 MB, the clusters’ dimension is 8 KB, meaning that the 1 KB files will occupy 8 KB of space on disk, because we cannot store multiple files in a cluster. In conclusion, we have 7 KB lost.
To solve this problem, FAT 32 emerged, a system that uses smaller cluster sizes and offers support for partitions up to 2 TB.
Notes: 8.3 filename.txt

## Slide 11: FAT32
It is generally accepted that the rule of thumb for selecting cluster size is “smaller is better”. Since FAT16 partitions wasted a lot of disk space, the move to FAT32 to reduce cluster size was immediate.
However, FAT32 also has its limitations. Consider a partition of less than 2,048 MB (2 GB), the largest that FAT16 can offer. If this partition is formatted using FAT16, it will result in a file allocation table with 65,526 clusters in it, each cluster consuming 32 KB.
Large cluster size will result in wasted disk space. Thus, it is recommended that this partition use FAT32, which will result in a cluster size of only 4 KB. This will result in up to 90% less disk space wasted.

## Slide 12: FAT 32
However, there is a price to pay for this. Since each cluster is smaller, there must be more of them to cover the same disk capacity.
So instead of 65,526 clusters, we will have 524,208 (65,526 * 8) clusters.
Furthermore, the FAT entries in the FAT32 table are 32 bits in size, compared to the 16-bit entries in FAT16. The end result is that the FAT table size is 16 times larger in FAT32 than in FAT16! The following table illustrates these observations:

## Slide 13: FAT16 and FAT32 characteristics
Type of FAT | FAT16 | FAT32
Cluster dimension | 32 KB | 4 KB
Number of FAT entries | 65,526 | 524,208
FAT table dimension | ~ 128 KB | ~ 2 MB

## Slide 14: FAT16 and FAT32 characteristics
Almost any OS is implementing a disk caching mechanism to keep in memory the disk structures frequently accessed (the FAT table, for example). The caching operation implies using the main memory to store information about disk, avoiding permanently reading from hard disk (very slow comparative with main memory).
So, when the FAT table is small (128 KB for FAT16) it is easy to store it in memory, but when the dimension of table grows up, the system is forced to use a big amount of memory for FAT, or not to use memory at all.

## Slide 15: FAT16 and FAT32 characteristics
For this reason, the FAT table size limit must be reduced to a reasonable size. In most cases, it is a matter of choosing a balance between cluster size and FAT size (the best example being FAT32).
Since FAT32 can have (at most) about 268 million clusters, a cluster size of 4 KB is technically capable of supporting a 1 TB disk. The only problem is that in this case, the FAT table size will be over 1 GB! (268 million multiplied by 4 bytes for each table entry).
Thus, FAT32 uses 4 KB clusters for volumes up to 8 GB in size, then uses larger clusters, as in the following table:

## Slide 16: The clusters’ dimensions for FAT32
Cluster dimension | The minimum dimension of the partition | The maximum dimension of the partition
4 KB | 0.5 GB | 8 GB
8 KB | 8 GB | 16 GB
16 KB | 16 GB | 32 GB
32 KB | 32 GB | 64 GB

## Slide 17: FAT32 characteristics
In the following table we may see the dimensions of the FAT table in MB, function of the partition’s dimension for different sizes of the clusters. We may see that FAT32 is using clusters of 4 KB until 8 GB partitions, otherwise the memory used to store FAT table would be too big.
The entries marked with bold show us what FAT32 Windows will choose for a partition of that size (the FAT table dimension is kept at 8 MB).

## Slide 18: The FAT32 table dimension
Partition dimension | 4 KB clusters | 8 KB clusters | 16 KB clusters | 32 KB clusters
8 GB | 8 MB | 4 MB | 2 MB | 1 MB
16 GB | 16 MB | 8 MB | 4 MB | 2 MB
32 GB | 32 MB | 16 MB | 8 MB | 4 MB
64 GB | 64 MB | 32 MB | 16 MB | 8 MB
2 TB (2,048 GB) | -- | 1,024 MB | 512 MB | 256 MB

## Slide 19: exFAT (Extensible File Allocation Table)
exFAT represents a file system introduced by Microsoft in 2006, optimized for use with flash memory devices such as USB sticks, SD (Secure Digital) cards or similar portable media.
Proprietary standard until 2019, when Microsoft made its specifications public.
exFAT solves the problem of FAT32 not being able to store files larger than 4GB, being the default file system (SD association) for SDXC cards with capacities greater than 32GB.

## Slide 20: ReFS – Resilient File System
Introduced by Microsoft in Windows Server 2012, also available in Windows 10/11 Pro Workstation
Designed for large data volumes, storage servers, and mission-critical environments
Advantages over NTFS:
  Automatic data integrity – checksums for each block, automatic corruption detection and correction
  Maximum scalability – volumes up to 1 yottabyte (YB), files up to 16 exabytes
  CHKDSK-free resiliency – no need for periodic disk scans
  Compatible with Storage Spaces – software RAID built into Windows
ReFS limitations:
  Does not support NTFS compression, EFS, transactions, hard links
  Cannot be used as boot partition (C:\)

## Slide 21: NTFS – New Technology File System
Starting with Win 2000, the NTFS file system is the native file system on Windows. NTFS is using 64 bits for index clusters.
This capability offers the ability to address volumes up to 16 exabytes.
Multiples of bytes |  |  |  | 
SI decimal prefixes |  | Binary usage |  | 
Name (Symbol) | Value |  |  | 
kilobyte (kB) | 103 | 210 |  | 
megabyte (MB) | 106 | 220 |  | 
gigabyte (GB) | 109 | 230 |  | 
terabyte (TB) | 1012 | 240 |  | 
petabyte (PB) | 1015 | 250 |  | 
exabyte (EB) | 1018 | 260 |  | 
zettabyte (ZB) | 1021 | 270 |  | 
yottabyte (YB) | 1024 | 280 |  | 

## Slide 22: NTFS characteristics
NTFS characteristics | Importance
Access control | Access rights for individual files or directories
MFT (Master File Table) | It contains records for each file and directory in NTFS; The records regarding NTFS structure and MFT are redundant when the first record is corrupted; Small files (under 1500 bytes) are stored entirely in MFT for a faster access.
NTFS file attributes | The file attributes are contained in the MFT record of the file. The list of the file attributes may be particularized for some other systems (Mac, UNIX, Linux) in order to extend the NTFS functionality.
Filenames | NTFS allows filenames up to 255 characters but it can generate 8+3 names for backward compatibility with FAT/DOS
Notes: abcdef~1.txt
abcdef~2.txt

## Slide 23: NTFS characteristics
POSIX compliance | The POSIX compliance enables UNIX apps to access the files stored in NTFS under Windows NT. To do this, NTFS needs some file attributes that are unique to POSIX, like: - Case sensitive filenames; - Hard-links that enable a file to be accessed from different sources; - A “time stamp" attribute to identify when a file was last accessed or modified.
Macintosh support | Macintosh support services enable users accessing files from Macintosh platforms; for Mac users the NT server looks like an AppleShare server. Macintosh access control rights are also supported.

## Slide 24: NTFS characteristics
Hot Fixing | If NTFS finds a bad sector on a SCSI disk will automatically move affected files and will mark it as "bad" without user intervention.
Filesystem recovery | NTFS is using the cache memory manager for buffer writes on disk within a process called "lazy-write". Alco, it runs a monitoring program for writing on the disk which allows to recover the filesystem in case of a crash. (https://docs.microsoft.com/en-us/windows/win32/fileio/file-caching)

## Slide 25: Master File Table - NTFS
Increased reliability by MFT special design

## Slide 26: MFT - characteristics
The Master File Table was been designed for a quick and safe access to files. The main characteristics of it are: superior performance in finding files on disk (quick find for small files and directories) and great reliability (as a result of redundant characteristics).
MFT can serve both objectives very well. First of all, the definition of MFT records enable small files and directories to be included in these records and there is not necessary any access to disk. For big files NTFS uses a hierarchical binary tree structure in order to quick search in bigger directories.
The reliability is assured by the link between these redundant characteristics:
  Redundant master record – the mirror record (the copy) of MFT;
  Redundant files and data segments MFT – mirror MFT;
  Redundant sector boots (the existence of the primary boot sector and dual boot sector – its copy).

## Slide 27: Comparison of NTFS and FAT File Systems
https://docs.microsoft.com/en-us/previous-versions/windows/it-pro/windows-vista/cc766145(v=ws.10)
(A good comparison between NTFS, FAT16 and FAT32)

## Slide 28: Modern Linux filesystems
Btrfs (B-tree FS) – default in Fedora (from 2020) and openSUSE:
Snapshots and instant rollback – you may come back to a previous state of the filesystem
Integrated RAID, transparent compression, data deduplication
ZFS – used on Ubuntu Server, FreeBSD, TrueNAS:
Storage pools, end-to-end checksums, automate self-healing
Industrial Standard for NAS (Network Attached Storage)
XFS – default on RHEL/CentOS/Rocky Linux:
Excellent performance for big files
Used on production servers and supercomputers
ext4 is the minimum today. Modern distributions are migrating to Btrfs/XFS.

## Slide 29: Modern Linux commands – disks and filesystems
lsblk – viewing disks and partitions structure
$ lsblk
$ lsblk -f #list filesystem on each partition
findmnt – viewing mounted filesystems
$ findmnt
$ findmnt --df # similar with df
ncdu – interactive version of du
$ ncdu /home # interactive space navigation

## Slide 30: Modern Linux commands – disks and filesystems
df și du :
$ df -h # free space for each partition (human readable)
$ df -T # list also the filesystem type
$ du -sh * # each dir dimension from the current directory
$ du -sh /* 2>/dev/null | sort -rh | head -10 # top 10 large directories

## Slide 31: Other filesystems
Default filesystem on a Linux is ext3 (third extended filesystem) or ext4 – More information at:
http://en.wikipedia.org/wiki/Ext3
http://en.wikipedia.org/wiki/Ext4
JFS (Journaling FileSystem) - filesystem created by IBM; used on Unix AIX and on Linux versions. “A journaling file system is a file system that keeps track of changes not yet committed to the file system's main part by recording the intentions of such changes in a data structure known as a "journal", which is usually a circular log.”
OCFS2 (Oracle Cluster File System) – filesystem created by Oracle for Linux clusters.
https://oss.oracle.com/projects/ocfs2/

## Slide 32: Which Linux file system should you choose?
Interesting video: Which is the best filesystem (for Linux) in 2024?
https://youtu.be/AhjL1SHku7M

## Slide 33: Unix/Linux commands about hard disk and partitions
df (disk free) – used to see the free space on a hard disk
df –h (human readable format)
du (disk usage) – used to determine the occupied space by a directory as a number of 512 bytes blocks
du –k (occupied space in blocks of 1 KB)
du –k | tail -1 (showing the last line of the listing – total no of blocks)

## Slide 34: Backup commands, file archiving-Linux
File archiving is used when one or more files need to be transmitted or stored as efficiently as possible. There are two aspects to this:
Archiving – Combining multiple files into one, which eliminates the overhead in individual files and makes it easier to transmit
Compressing – Making the files smaller by removing redundant information
You can archive multiple files into a single archive and then compress it, or you can compress an individual file. The former is still referred to as archiving, while the latter is just called compression.
When you take an archive, decompress it and extract one or more files, you are un-archiving it.

## Slide 35: Compressing files
Compressing files makes them smaller by removing duplication from a file and storing it such that the file can be restored.
When talking about compression, there are two types:
Lossless: No information is removed from the file. Compressing a file and decompressing it leaves something identical to the original.
Lossy: Information might be removed from the file as it is compressed so that uncompressing a file will result in a file that is slightly different than the original. For instance, an image with two subtly different shades of green might be made smaller by treating those two shades as the same. Often, the eye can’t pick out the difference anyway.

## Slide 36: Compressing files
From lossy compression often benefits media because the results are smaller files in size and people can’t tell the difference between the original and the version with the changed data.
For things that must remain untouched (documents, logs, and software) you may need lossless compression.
Most image formats, such as GIF (Graphics Interchange Format ), PNG (Portable Network Graphics), and JPEG (Joint Photographic Experts Group), implement some kind of lossy compression.

## Slide 37: Tar archiving command
tar (tape archive) –standard for all Unix versions
  General syntax:
tar function [modifier] destination_file(s) | directories
tar functions:
  c (create) – in order to create an archive
  t (table of contents) – in order to view the content table of a tar file
  x (extract) – used to extract files from archive
Modifiers (a few examples):
  f (filename) – the tar file will be created; otherwise it is picked the device specified by the medium variable TAPE, if it is set; if not, the default value from /etc/default/tar is used.
  v (verbose) – together with the t function gives extra information about tar file

## Slide 38: Archiving and compression commands
tar examples:
- tar -cvf dir2backup.tar dir2 (it creates the tar archive for dir2 directory)
- tar -cvf ex.tar f1 f2 f3 (it creates the tar archive with files f1, f2, f3)
tar -tvf ex.tar (to view the contents of an archive)
tar -xvf myfile.tar (extraction from the tar file)
tar –zcvf mybackups/udev.tar.gz /etc/udev (To create a tar file that is compressed use -z option: The -z option makes use of the gzip utility to perform compression)
tar -czf a_files.tar.gz a*
To add a file to an existing archive, use the -r option to the tar command:
tar -rvf udev.tar /etc/hosts
The modern alternative for incremental backup is rsync – it transfers only changed files, works locally and via SSH:
rsync -avh --progress /home/user/ /backup/user/

## Slide 39: Compression commands- UNIX/Linux
GNU compression program: gzip
The gzip creates a smaller file with .gz extension. For example, the command:
gzip student
the student file will be transformed into a compressed file called student.gz
gzip –l student.gz
will offer information about the compression ratio
gunzip (gzip –d) is used for decompression
Note: We may find on Linux the zip and unzip commands, similar with Windows versions. In this case we may work with zip files compressed on Windows.
zip home.zip * - will create an archive called home.zip from all files in the present working directory
The command: unzip labs.zip will extract all the files from the archive to the current directory
unzip –l labs.zip will list the files in the .zip archives

## Slide 40: Compression commands- UNIX/Linux
Other compression commands are bzip2 and xz:
The bzip2 command uses Burrows-Wheeler compression algorithm which will compress files smaller than gzip at the expense of more CPU time. The resulted files have a .bz2 extension, instead of .gz extension.
xz command: it’s similar with gzip and it uses the Lempel-Ziv-Markov (LZMA) algorithm. It can provide a better compression ratio than bzip2.
The files compressed with the xz command use .xz extension.
In order to uncompress the .xz file, unxz command can be used
(or xz –d).

## Slide 41: Zstd compression
zstd (Zstandard) – modern algorithm for compression (Facebook, 2015):
5x faster than gzip better compression ratio
Used in Linux kernel, Facebook, Android, modern archives like .deb/.rpm
$ zstd fisier.tar # compression → fisier.tar.zst
$ zstd -d fisier.tar.zst # decompression
$ tar -I zstd -cvf arhiva.tar.zst director/
Compression algorithms comparison:
gzip (1992) → bzip2 (1996) → xz/LZMA (2005) → zstd (2016) ← modern standard

## Slide 42: PowerShell commands for Windows –equivalents for df, du
df -h Windows equivalent:
Get-PSDrive -PSProvider FileSystem
# Or:
Get-Volume | Select DriveLetter,FileSystem,Size,SizeRemaining
Partitions – detailed information:
Get-Partition | Select DiskNumber,PartitionNumber,Size,Type
Graphical tool: WinDirStat
  WinDirStat – visual heatmap of disk space usage, free
  Download: https://windirstat.net